## Slide 1: A Fast Estimation of SRAM Failure Rate Using Probability Collectives
Fang Gong
Electrical Engineering Department, UCLA
http://www.ee.ucla.edu/~fang08
Collaborators: Sina Basir-Kazeruni, Lara Dolecek, Lei He
{fang08, sinabk, dolecek, lhe}@ee.ucla.edu

## Slide 2: Outline
Background
Proposed Algorithm
Experiments
Extension Work

## Slide 3: Background
Variations
Static Variation
Dynamic Variation
Process Variation
Voltage Variation
Temperature Variation

## Slide 4: Rare Failure Event
Rare failure event exists in highly replicated circuits:
  SRAM bit-cell, sense amplifier, delay chain and etc.
  Repeat million times to achieve high capacity.
  Process variation lead to statistical behavior of these circuits.
Need extremely low failure probability:
  Consider 1Mb SRAM array including 1 million bit-cells, and we desire 99% yield for the array*:
    99.999999% yield requirement for bit-cells.
  Failure probability of SRAM bit-cell should < 1e-8!
  Circuit failure becomes a “rare event”.
* Source: Amith Singhee, IEEE transaction on Computer Aided Design (TCAD), Vol. 28, No. 8, August 2009

## Slide 5: Problem Formulation
Given Input:
  Variable Parameters  probabilistic distributions;
  Performance constraints;
Target Output:
  Find the percentage of circuit samples that fail the performance constraints.
Design
Parameters
Process
Parameters
Random
Distribution
Fixed
Value
Circuit
Performance
Measurements or SPICE engine
Failure
Probability

## Slide 6: Monte Carlo Method for Rare Events
Required time in order to achieve 1% relative error
Assumes 1000 SPICE simulations per second!
Rare Event Probability | Simulation Runs | Time
1e-3 | 1e+7 | 16.7mins
1e-5 | 1e+9 | 1.2 days
1e-7 | 1e+11 | 116 days
1e-9 | 1e+13 | 31.7 years
Monte Carlo method for rare events
(Courtesy: Solido Design Automation)

## Slide 7: Importance Sampling
Basic Idea:
  Add more samples in the failure or infeasible region.
How to do so?
  IS changes the sampling distribution so that rare events become “less-rare”.
Importance Sampling Method*
*Courtesy: Solido Design Automation

## Slide 8: Mathematic Formulation
Indicator Function
Probability of rare failure events
  Random variable x and its PDF h(x)
  Likelihood ratio or weights for each sample of x is
Success Region
Failure Region (rare failure events)
I(x)=0
I(x)=1
prob(failure) =
spec

## Slide 9: Key Problem of Importance Sampling
Q: How to find the optimal g(x) as the new sampling distribution?
A: It has been given in the literature but difficult to calculate:

## Slide 10: Outline
Background
Proposed Algorithm
Experiments
Extension Work
* Proposed algorithm is based on several techniques. Due to limited time, we only present the overall algorithm in this talk. More details can be found in the paper.

## Slide 11: Basic Idea
Find one parameterized distribution to approximate the theoretical optimal sampling distribution as close as possible.
Modeling of process variations in SRAM cells:
  VTH variations are typically modeled as independent Gaussian random variables;
  Gaussian distribution can be easily parameterized by:
    mean value  mean-shift : move towards failure region.
    standard-deviation  sigma-change: concentrate more samples around the failure region.
  parameterized Gaussian distribution  the optimal sampling distribution.

## Slide 12: Find the Optimal Solution
Need to solve an optimization problem:
  Minimize the distance between the parameterized distribution and the optimal sampling distribution.
Three Questions:
  What is the objective function?
    e.g., how to define the distance?
  How to select the initial solution of parameterized distributions?
  Any analytic solution to this optimization problem?

## Slide 13: Objective Function
Kullback-Leibler (KL) Distance
  Defined between any two distributions and measure how “close” they are.  “distance”
Optimization problem based on KL distance
With the parameterized distribution, this problem becomes:

## Slide 14: Initial Parameter Selection
It is important to choose “initial solution” of mean and std-dev for each parameterized distribution.
Find the initial parameter based on “norm minimization”
  The point with “minimum L2-norm” is the most-likely location where the failure can happen.
  The figure shows 2D case but the same technique applies to high-dim problems.
Parameter 1
Parameter 2
Nominal point
Failure region

## Slide 15: Analytic Optimization Solution
Recall that the optimization problem is
  Eh cannot be evaluated directly and sampling method must be used:
Above problem can be solved analytically:
  follows Gaussian distribution
  The optimal solution of this problem can be solved by (e.g., mean):
Analytic Solution

## Slide 16: Overall Algorithm
Input random variables with given distribution
Step1: Initial Parameter Selection
(1) Draw uniform-distributed samples
(2) Identify failed samples and calculate their L2-norm
(3) Choose the value of failed sample with minimum L2-norm as the initial ; set as the given
Step2: Optimal Parameter Finding
Draw N2 samples from parameterized distribution and set iteration index t=2
Run simulations on N2 samples and evaluate
converged?
Return
Yes
No
Draw N2 samples from

## Slide 17: Overall Algorithm (cont.)
Step3: Failure Probability Estimation
Draw N3 samples from parameterized distribution
Run simulations on N3 samples and evaluate indicator function
Return the failure probability estimation
Solve for the failure probability with sampled form as
where

## Slide 18: Outline
Background
Proposed Algorithm
Experiments
Extension Work

## Slide 19: 6-T SRAM bit-cell
SRAM cell in 45nm process as an example:
  Consider VTH of six MOSFETs as independent Gaussian random variables.
  Std-dev of VTH is the 10% of nominal value.
Performance Constraints:
  Static Noise Margin (SNM) should be large than zero;
  When SNM<=0, data retention failure happens (“rare events”).

## Slide 20: Accuracy Comparison (Vdd=300mV) - Evolution of the failure rate estimation
Failure rate estimations from all methods can match with MC;
Proposed method starts with a close estimation to the final result;
Importance Sampling is highly sensitive to the sampling distribution.

## Slide 21: Efficiency Comparison (Vdd=300mV) - Evolution of figure-of-merit (FOM)
Figure-of-merit is used to quantify the error (lower is better):
Proposed method can improve accuracy with1E+4 samples as:
90% accuracy level
 | MC | MixIS | SS | Proposed
Probability of failure | 5.455E-4 | 3.681E-4 | 4.343E-4 | 4.699E-4
Accuracy | 18.71% | 88.53% | 90.42% | 98.2%

## Slide 22: Outline
Background
Proposed Algorithm
Experiments
Extension Work

## Slide 23: Problem of Importance Sampling
Q: How does Importance Sampling behave for high-dimensional problems (e.g., tens or hundreds variables)?
A: Unreliable or completely wrong!
 curse of dimensionality
Reason: the degeneration of likelihood ratios
  Some likelihood ratios become dominate (e.g., very large when compared with the rest)
  The variance of likelihood ratios are very large.
prob(failure)

## Slide 24: Extension Work
We develop an efficient approach to address rare events estimation in high dimension which is a fundamental problem in multiple disciplines.
Our proposed method can reliably provide high accuracy:
  tested problem with 54-dim and 108-dim;
  probability estimation of rare events can always match with MC method;
  It provides several order of magnitude speedup over MC while other IS-based methods are completely failed.
We can prove that IS method loses its upper bound of estimation in high-dimension, and estimation from our method can always be bounded.
Study Case |  | Monte Carlo (MC) | Spherical Sampling | Proposed Method
108-dim | P(fail) | 3.3723e-05 | 1.684 | 3.3439e-005
 | Relative error | 0.097354 | 0.09154 | 0.098039
 | #run | 5.7e+6 (1425X) | 4.3e+4 | 4e+3 (1X)

## Slide 25: Thank you! Any further questions can be addressed to fang08@ee.ucla.edu