Last week I rerun the experiment with the updated Ptrace. With the new Ptrace, the delay estimation is much more accurate. The Figure 1 shows the delay comparison under the device setting Vdd=0.9, Vt=0.3, the delay error is within 4% for all benchmarks, and the average error is only 0.8%. Figure 2 shows the energy comparison. The energy error is within 5% and the average energy error is only 1.2%.

Figure 1

Figure 2

The following table shows the min-ED hyper-archs for each class. The min-ED hyper-archs are not exactly the same as the previous ones, however, the ED reduction compared to the baseline is similar compared to the previous result.

| Hyper-arch Class | Vdd (V) | CVt (V) | Ivt (V) | (N,K) | Energy (nJ) | Delay (ns) | ED (nJ·ns) | ED Reduction % | Normalized Area % |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Baseline | 0.9 | 0.30 | 0.30 | (8,4) | 1.20 | 23.5 | 28.2 | - | 100.00 |
| Hemo-Vt | 1.0 | 0.30 | 0.30 | (10,4) | 1.37 | 17.5 | 24.1 | 14.54 | 81.90 |
| Hetero-Vt | 0.9 | 0.25 | 0.30 | (12,4) | 1.27 | 18.1 | 23.0 | 18.44 | 79.52 |
| Hemo-Vt+G | 0.9 | 0.25 | 0.25 | (12,4) | 0.74 | 16.10 | 11.9 | 57.80 | 127.43 |
| Hetero-Vt+G | 0.8 | 0.25 | 0.20 | (10,4) | 0.65 | 17.30 | 11.2 | 60.28 | 126.19 |