Summary of primary results

Two types of cost function have been tried.

(1)

(2)

It turns out that cost function (1) with criticality exponent 0.4 leads to the smallest mean and standard deviation of circuit delay.

When the variation setting is 10%/10%/10% as 3sigma for global/local/spatial variation, on average ST-VPlace reduces the mean and standard deviation of circuit delay by 3.33% (up to 10%) and 5.63% (up to 17%)  respectively compared to T-VPlace. Using the same 3sigma guard-banded delay as the cut-off delay, ST-VPlace achieves a 9.42X (up to 142X) smaller yield loss. If holding the same yield loss, ST-VPlace reduces the reported delay by 4.10% (up to 9%). ST-VPlace consistently achieves a smaller yield loss compared to T-VPlace with different guard-band factors under different variations.

ST-VPlace consistently achieves a smaller yield loss compared to T-VPlace with speed-binning under different variations. A larger variation leads to a larger yield loss. It’s due to two reasons. Firstly, the ignored with-in die variation (local and spatial) is larger. Secondly, the inaccuracy due to the fact that the nominal value in STA is smaller than the mean value in SSTA is larger. When the relaxed factor is 10%, ST-VPlace reduces yield loss by 9.73X and 5.85X under variation 5%/5%/5% and 10%/10%/10% as 3 sigma for global/local/spatial variation respectively. Details are as follows.

i) Cost function tuning for stochastic placement considering spatial variation

Two timing cost function have been tried. The first one is

The following figure shows the geometric mean of mean delay and standard deviation of delay for 20 MCNC designs. The variation setting is 10%/10%/10% as 3sigma for global/local/spatial variation unless otherwise specified. Seven candidates from 0.1 to 0.7 have been tried for the criticality exponents. It’s clear that theta=0.4 leads to the smallest mean and standard deviation.

The second cost function is as

where sigma_d(i, j) is the standard deviation for each connection (i, j). Seven candidates from 0.1 to 0.7 have also been tried for the criticality exponents. The following figure shows the geometric mean for mean delay and standard deviation of circuit delay over 20 MCNC designs. We can see that theta = 0.4 still leads to the smallest mean and but not the deviation. In addition, the curves fluctuate much more.

We compare two cost function tuning curves as following.

For theta = 0.4, the two cost functions have almost the same mean but the first type of cost function leads to a 3% smaller standard deviation. In the following, we use the first type of cost function.

ii) Comparison of ST-VPlace and T-VPlace considering spatial variation

The variation setting is 10%/10%/10% as 3sigma for global/local/spatial variation.

|  | T-Vplace | ST-Vplace |
| --- | --- | --- |
| circuit | # of CLBs | Tnorm (ns) | Tgrd (ns) | Tmean (ns) | Tsigma (ns) | YLgrd (pp10K) | Tmean (ns) | Tsigma (ns) | Tst-v (ns) | YLst-v (pp10K) |
| alu4 | 162 | 17.80 | 29.10 | 19.14 | 2.59 | 0.62 | 18.50 | 2.56 | 28.33 | 0.17 |
| apex2 | 213 | 22.20 | 34.50 | 22.60 | 3.34 | 1.87 | 21.80 | 2.99 | 32.45 | 0.11 |
| apex4 | 134 | 17.80 | 27.10 | 18.63 | 2.41 | 2.21 | 18.70 | 2.49 | 27.45 | 3.73 |
| bigkey | 294 | 10.40 | 15.60 | 11.52 | 1.44 | 23.17 | 11.30 | 1.29 | 14.96 | 4.43 |
| clma | 1358 | 38.00 | 60.50 | 40.17 | 5.42 | 0.89 | 37.40 | 5.08 | 56.42 | 0.03 |
| des | 218 | 17.99 | 30.35 | 21.07 | 3.13 | 15.10 | 20.96 | 3.16 | 30.34 | 14.94 |
| diffeq | 195 | 23.50 | 45.40 | 26.75 | 5.27 | 2.04 | 25.80 | 4.39 | 41.32 | 0.04 |
| dsip | 162 | 9.51 | 16.00 | 10.60 | 2.06 | 43.15 | 10.70 | 1.77 | 15.34 | 13.39 |
| elliptic | 421 | 31.60 | 53.40 | 33.57 | 5.34 | 1.03 | 30.20 | 5.09 | 49.11 | 0.03 |
| ex1010 | 493 | 25.40 | 36.70 | 26.54 | 3.22 | 8.14 | 26.40 | 3.18 | 36.42 | 5.99 |
| ex5p | 123 | 19.00 | 30.40 | 20.43 | 2.76 | 1.47 | 19.40 | 2.66 | 29.02 | 0.17 |
| frisc | 595 | 39.30 | 71.20 | 42.44 | 7.19 | 0.31 | 42.30 | 7.22 | 71.19 | 0.31 |
| misex3 | 153 | 18.20 | 30.15 | 19.53 | 2.77 | 0.63 | 18.29 | 2.41 | 27.54 | 0.00 |
| pdc | 568 | 25.30 | 39.80 | 27.31 | 3.39 | 1.15 | 26.80 | 3.31 | 39.00 | 0.43 |
| s298 | 256 | 38.25 | 62.50 | 39.60 | 6.03 | 0.74 | 36.90 | 5.62 | 58.24 | 0.03 |
| s38417 | 847 | 24.02 | 42.54 | 29.13 | 4.04 | 4.53 | 27.49 | 3.89 | 40.41 | 0.56 |
| s38584 | 704 | 19.69 | 32.62 | 20.60 | 3.45 | 2.51 | 20.34 | 3.26 | 31.68 | 0.83 |
| seq | 198 | 16.80 | 26.80 | 18.17 | 2.35 | 1.22 | 17.90 | 2.30 | 26.36 | 0.56 |
| spla | 399 | 26.00 | 37.40 | 26.71 | 3.33 | 6.58 | 24.90 | 3.03 | 34.64 | 0.19 |
| tseng | 131 | 22.10 | 38.10 | 23.48 | 4.17 | 2.29 | 23.20 | 4.04 | 37.37 | 1.14 |
| geo | 295.92 | 21.71 | 35.40 | 23.43 | 3.42 | 2.37 | 22.65 (-3.33%) | 3.23 (-5.63%) | 33.95 (-4.10%) | 0.36 (9.42X ) |

Interpretation of each column

| Tnorm | The nominal delay by STA in T-VPlace |
| --- | --- |
| Tgrd | The 3 sigma guard-banded delay by STA in T-VPlace |
| YLgrd | The yield loss in pp10K in T-VPlace analyzed by SSTA using Tgrd as the cut-off delay |
| Tmean | The mean delay by SSTA in T-VPlace/ST-VPlace |
| Tsigma | The standard deviation of delay by SSTA in T-VPlace/ST-VPlace |
| Tst-v | The delay in ST-VPlace is holding the same yield loss as YLgrd |
| YLst-v | The yield loss in pp10K in ST-VPlace analyzed by SSTA using Tgrd as the cut-off delay |

From the above table, we can see that on average ST-VPlace reduces the mean and standard deviation of circuit delay by 3.33% (up to 10%) and 5.63% (up to 17%)  respectively compared to T-VPlace. Using the same 3sigma guard-banded delay as the cut-off delay, ST-VPlace achieves a 9.42X (up to 142X) smaller yield loss. If holding the same yield loss, ST-VPlace reduces the reported delay by 4.10% (up to 9%).

The following figure compares the normalized mean and standard deviation of circuit delay for 20 MCNC designs in ST-VPlace. Both of the mean and deviation are normalized to their counterpart in T-VPlace. It’s clear that ST-VPlace achieves a smaller mean and deviation for most of the designs.

ii) Effect of guard-banding

The above two figures shows the yield loss by T-VPlace and ST-VPlace with different guard-band factors under different variation settings. The variation settings are 5%/5%/5% and 10%/10%/10% as 3sigma for global/local/spatial variation respectively. A larger variation leads to a larger guard-band cost with a same guard-band factor. With the same guard-band factor, the yield loss in T-VPlace is similar under different variation settings. ST-VPlace consistently achieves a smaller yield loss compared to T-VPlace. Under the same variation, the gain of ST-VPlace over T-VPlace increases with a larger guard-band factor. With the same guard-band factor, the gain of ST-VPlace over T-VPlace decreases with a larger variation setting. The cost and yield loss are based on the arithmetic mean and geometric mean over 20 MCNC designs respectively.

ii) Effect of speed-binning

We arbitrarily partition the bins such that the fast/medium/slow bin contains 40%/30%/29.999% chips. The slowest 0.0001% (0.1pp10K) chips are always discarded. The timing specification for each bin may be relaxed by 0% to 20%. The above two figures show that the yield loss in T-VPlace and ST-VPlace with different relaxed factors under different variations. The data are based on the geometric mean over MCNC designs. It’s clear that ST-VPlace consistently achieves a smaller yield loss compared to T-VPlace. A larger variation leads to a larger yield loss. It’s due to two reasons. Firstly, the ignored with-in die variation (local and spatial) is larger. Secondly, the inaccuracy due to the fact that the nominal value in STA is smaller than the mean value in SSTA is larger. When the relaxed factor is 10%, ST-VPlace reduces yield loss by 9.73X and 5.85X under variation 5%/5%/5% and 10%/10%/10% as 3 sigma for global/local/spatial variation respectively.