i) Comparison of ST-VPlace w/ and w/o spatial variation

|  | T-VPlace | ST-VPlace w/o spatial | ST-VPlace w/ spatial |
| --- | --- | --- | --- |
| Yield loss (pp10K) | 2.37 | 0.54 | 0.36 |
| Runtime | 1X | 1.29X | 2.86X |

The above table summarizes the comparison and the details are as below.

The following table compares the stochastic placement w/ and w/o spatial variation. Both are evaluated w/ spatial variation. ST-VPlace w/ spatial variation achieves the same mean delay but reduces the standard deviation by 2.5% on average compared to the one w/o spatial variation. This leads to a 0.18pp10K (up to 12.7 pp10K) yield loss reduction.

| circuit | T-Vplace | ST-Vplace |
| --- | --- | --- |
|  |  | w/ spatial | w/o spatial |
|  | Tgrd | Tmean | Tsigma | Ylst-v(pp10K) | Tmean | Tsigma | Ylst-v(pp10K) |
| alu4 | 29.10 | 18.50 | 2.56 | 0.17 | 18.84 | 2.64 | 0.50 |
| apex2 | 34.50 | 21.80 | 2.99 | 0.11 | 21.19 | 2.93 | 0.03 |
| apex4 | 27.10 | 18.70 | 2.49 | 3.73 | 18.75 | 2.50 | 4.20 |
| bigkey | 15.60 | 11.30 | 1.29 | 4.43 | 11.52 | 1.38 | 15.45 |
| clma | 60.50 | 37.40 | 5.08 | 0.03 | 37.87 | 5.12 | 0.05 |
| des | 30.35 | 20.96 | 3.16 | 14.94 | 21.15 | 3.05 | 12.99 |
| diffeq | 45.40 | 25.80 | 4.39 | 0.04 | 25.38 | 4.67 | 0.09 |
| dsip | 16.00 | 10.70 | 1.77 | 13.39 | 9.84 | 2.05 | 13.47 |
| elliptic | 53.40 | 30.20 | 5.09 | 0.03 | 31.39 | 5.31 | 0.17 |
| ex1010 | 36.70 | 26.40 | 3.18 | 5.99 | 25.76 | 3.13 | 2.33 |
| ex5p | 30.40 | 19.40 | 2.66 | 0.17 | 18.92 | 2.55 | 0.03 |
| frisc | 71.20 | 42.30 | 7.22 | 0.31 | 42.01 | 7.00 | 0.15 |
| misex3 | 30.15 | 18.29 | 2.41 | 0.00 | 18.20 | 2.45 | 0.01 |
| pdc | 39.80 | 26.80 | 3.31 | 0.43 | 26.87 | 3.38 | 0.64 |
| s298 | 62.50 | 36.90 | 5.62 | 0.03 | 38.09 | 5.76 | 0.11 |
| s38417 | 42.54 | 27.49 | 3.89 | 0.56 | 29.52 | 4.33 | 13.26 |
| s38584.1 | 32.62 | 20.34 | 3.26 | 0.83 | 20.04 | 3.51 | 1.70 |
| seq | 26.80 | 17.90 | 2.30 | 0.56 | 18.15 | 2.37 | 1.31 |
| spla | 37.40 | 24.90 | 3.03 | 0.19 | 25.14 | 3.15 | 0.50 |
| tseng | 38.10 | 23.20 | 4.04 | 1.14 | 22.81 | 4.02 | 0.72 |
| geo | 35.40 | 22.65 | 3.23 | 0.36 | 22.66 | 3.31 | 0.54 |

As shown in the following table, compared to T-VPlace, the stochastic placement algorithms take 1.29X and 2.86X runtime w/o and w/ spatial variation, respectively.

| circuit | t-vplace | st-vplace |
| --- | --- | --- |
|  |  | w/o spatial | w/ spatial |
| alu4 | 16.82 | 27.74 | 59.16 |
| apex2 | 44.42 | 61.01 | 113.67 |
| apex4 | 29.55 | 32.72 | 58.4 |
| bigkey | 57.51 | 83.9 | 198.79 |
| clma | 586.72 | 739.02 | 2645.94 |
| des | 54.48 | 73.1 | 143.43 |
| diffeq | 42.64 | 60.95 | 99.05 |
| dsip | 41.89 | 54.18 | 96.15 |
| elliptic | 145.19 | 191.05 | 475.21 |
| ex1010 | 190.42 | 226.33 | 491.35 |
| ex5p | 26.31 | 31.52 | 56.64 |
| frisc | 216.42 | 279.46 | 877.75 |
| misex3 | 24.61 | 37.1 | 64.39 |
| pdc | 253.48 | 281.38 | 563.83 |
| s298 | 43.73 | 46.8 | 127.15 |
| s38417 | 268.26 | 340.16 | 1050.64 |
| s38584.1 | 230.97 | 294.47 | 877.49 |
| seq | 29.31 | 44.39 | 68.3 |
| spla | 109.43 | 93.99 | 278.42 |
| tseng | 15.91 | 23.43 | 51.26 |
| Geo. | 1X | 1.29X | 2.86X |

ii) Stochastic Routing: (S-Pathfinder) considering variations

- Cost function in Pathfinder

Considering the connection to sink j of net i, the cost to include a routing source n is

(1)

where the first term is the timing cost and the second term is for wire congestion. The static criticality is defined as

(2)

where MaxCrit is the maximum criticality that any connection can have, η is the criticality component. Both are the parameters to control how a connection’s slack impacts the congestion delay tradeoff in the cost function. Setting MaxCrit to 1 makes the nets on the critical path pay no attention to congestion. It has been shown that a MaxCrit of 0.99 can achieve a better routability without impact on circuit timing compared to a MaxCrit of 1. In addition, η of 1 leads to the best circuit timing.

PathCost(n) is the total cost of the path from the current partial routing tree to node n and is defined as

(3)

The total cost includes the expected cost from node n to target sink j and is defined as

(4)

It has been shown that an alpha of 1.2 leads to the best results.

- New cost function in S-Pathfinder

In order to consider variation in the stochastic router, we replace (2) with

(5)

Where SCriticality(i, j) is the probability that connection (i, j) is timing critical considering variation. Plug (5) into (1) and we have stochastic cost function as

(6)

Plug (6) into (3) and then (4) gives us the new cost function considering variations.

- S-Pathfinder development

Coding on S-Pathfinder has been finished, debugged and tested. The coding mainly includes

- for each net, route the statistically critical sink first instead of statically critical sink first

- After routing a net, instead of only updating the nominal delay for routing tree, calculate the delay in canonical form for the tree;

- After one iteration of routing, using SSTA instead STA for criticality analysis

- Ongoing work includes tuning the cost function and performing experiments