|  | w/o var | w/ var | delay reduction |
| --- | --- | --- | --- |
| alu4 | 1.782E-08 | 1.718E-08 | 3.62% |
| apex2 | 2.219E-08 | 2.127E-08 | 4.16% |
| apex4 | 1.778E-08 | 1.680E-08 | 5.49% |
| bigkey | 1.038E-08 | 9.843E-09 | 5.14% |
| clma | 3.805E-08 | 3.572E-08 | 6.13% |
| des | 1.799E-08 | 1.701E-08 | 5.44% |
| diffeq | 2.348E-08 | 2.225E-08 | 5.21% |
| dsip | 9.506E-09 | 8.971E-09 | 5.63% |
| elliptic | 3.161E-08 | 2.943E-08 | 6.88% |
| ex1010 | 2.539E-08 | 2.426E-08 | 4.45% |
| ex5p | 1.898E-08 | 1.806E-08 | 4.83% |
| frisc | 3.934E-08 | 3.792E-08 | 3.62% |
| misex3 | 1.820E-08 | 1.739E-08 | 4.43% |
| pdc | 2.534E-08 | 2.358E-08 | 6.97% |
| s298 | 3.825E-08 | 3.679E-08 | 3.82% |
| s38417 | 2.402E-08 | 2.315E-08 | 3.61% |
| s38584.1 | 1.969E-08 | 1.857E-08 | 5.70% |
| seq | 1.683E-08 | 1.623E-08 | 3.54% |
| spla | 2.604E-08 | 2.495E-08 | 4.18% |
| tseng | 2.206E-08 | 2.136E-08 | 3.19% |

There is some initial result for variation aware placement and route. The following table shows the critical path delay reduction by applying variation aware placement. The variation setting is: 3 sigma of inter-die, spatial, random, and orientation variation are 10%, 7%, 7%, and 3% of the nominal value respectively. From the table we can see that the delay reduction due to variation aware placement is about 5% for all benchmarks.

For the skew SSTA part, there is some initial derivation result which is shown in the scan in page.