i) Experimental results for stochastic routing

- Cost function tuning

The deterministic T-VPlace is used as the placement algorithm. We first tune the criticality exponent in the cost function. The following figure shows that exponent of 0.2 leads to the smallest mean and standard deviation of delay on average. The variation is 10%/10%/10% as 3sigma for global/local/spatial variation.

- Comparison between Pathfinder and S-Pathfinder

We compare the mean and deviation of S-Pathfinder and Pathfinder in the following figure. The mean and deviation of S-Pathfinder are normalized to their counterparts in Pathfinder, respectively. S-Pathfinder achieves smaller (as good as) mean and deviation for most designs. A smaller mean delay usually leads to a smaller deviation. On average, S-Pathfinder reduces mean and deviation of delay by 2% (up to 10%).

We compare the yield loss (in pp10K) in the following table.

|  | Pathfinder | S-Pathfinder |
| --- | --- | --- |
| circuit | Tgrd | Tmean | Tdev | Ylgrd (pp10K) | Tmean | Tdev | YL-s (pp10K) | TYL-s |
| alu4 | 29.10 | 19.14 | 2.59 | 0.62 | 18.96 | 2.56 | 0.37 | 28.79 |
| apex2 | 34.50 | 22.60 | 3.34 | 1.87 | 21.74 | 3.03 | 0.13 | 32.52 |
| apex4 | 27.10 | 18.63 | 2.41 | 2.21 | 19.02 | 2.45 | 4.88 | 27.63 |
| bigkey | 15.60 | 11.52 | 1.44 | 23.17 | 11.90 | 1.44 | 50.62 | 15.97 |
| clma | 60.50 | 40.17 | 5.42 | 0.89 | 38.37 | 5.18 | 0.10 | 57.78 |
| des | 30.35 | 21.07 | 3.13 | 15.10 | 20.88 | 3.14 | 12.81 | 30.19 |
| diffeq | 45.40 | 26.75 | 5.27 | 2.04 | 25.77 | 5.17 | 0.73 | 44.05 |
| dsip | 16.00 | 10.60 | 2.06 | 43.15 | 10.67 | 2.02 | 41.79 | 15.98 |
| elliptic | 53.40 | 33.57 | 5.34 | 1.03 | 31.09 | 5.16 | 0.08 | 50.24 |
| ex1010 | 36.70 | 26.54 | 3.22 | 8.14 | 25.85 | 3.11 | 2.43 | 35.65 |
| ex5p | 30.40 | 20.43 | 2.76 | 1.47 | 20.04 | 2.70 | 0.63 | 29.82 |
| frisc | 71.20 | 42.44 | 7.19 | 0.31 | 42.25 | 7.23 | 0.31 | 71.18 |
| misex3 | 30.15 | 19.53 | 2.77 | 0.63 | 18.75 | 2.64 | 0.08 | 28.87 |
| pdc | 39.80 | 27.31 | 3.39 | 1.15 | 27.23 | 3.42 | 1.19 | 39.83 |
| s298 | 62.50 | 39.60 | 6.03 | 0.74 | 38.28 | 5.86 | 0.18 | 60.52 |
| s38417 | 42.54 | 29.13 | 4.04 | 4.53 | 29.29 | 4.01 | 4.76 | 42.59 |
| s38584.1 | 32.62 | 20.60 | 3.45 | 2.51 | 20.34 | 3.48 | 2.10 | 32.45 |
| seq | 26.80 | 18.17 | 2.35 | 1.22 | 18.21 | 2.37 | 1.45 | 26.90 |
| spla | 37.40 | 26.71 | 3.33 | 6.58 | 23.94 | 3.03 | 0.04 | 33.67 |
| tseng | 38.10 | 23.48 | 4.17 | 2.29 | 23.43 | 4.18 | 2.25 | 38.08 |
| geo | 35.40 | 23.43 | 3.42 | 2.37 | 22.96 (-2%) | 3.35 (-2%) | 0.95 (2.5X) | 34.70 (-2%) |

The interpretation of each column is as

| Tgrd | The 3sigma guard-banded delay in Pathfinder |
| --- | --- |
| Tmean | The mean delay in Pathfinder/S-Pathfinder |
| Tdev | The standard deviation in Pathfinder/S-Pathfinder |
| YLgrd | The yield loss in Pathfinder using Tgrd as the cut-off delay |
| YL-s | The yield loss in S-Pathfinder using Tgrd as the cut-off delay |
| TYL-s | The delay in S-Pathfinder if holding the same yield loss in YLgrd in Pathfinder |

On average, S-Pathfinder reduces yield loss by 2.5X (up to 148X). If holding the same yield loss, S-Pathfinder reduces the reported delay by 2% (up to 10%).

Runtime comparison of Pathfinder and S-Pathfinder is presented in the following table.

| Circuit | Pathfinder | S-Pathfinder |
| --- | --- | --- |
|  | runtime | # of iterations | runtime | # of iterations |
| alu4 | 9.18 | 18 | 9.07 | 14 |
| apex2 | 28.66 | 22 | 28.95 | 18 |
| apex4 | 16.92 | 25 | 14.58 | 15 |
| bigkey | 33.82 | 18 | 36.82 | 11 |
| clma | 369.27 | 23 | 330.91 | 12 |
| des | 30.96 | 21 | 29.86 | 14 |
| diffeq | 25.34 | 20 | 26.25 | 19 |
| dsip | 23.93 | 15 | 25.3 | 13 |
| elliptic | 79.5 | 24 | 74.25 | 13 |
| ex1010 | 111.06 | 28 | 99.49 | 18 |
| ex5p | 15.1 | 27 | 12.57 | 14 |
| frisc | 131.02 | 21 | 123.76 | 13 |
| misex3 | 14.33 | 18 | 15.32 | 15 |
| pdc | 136.68 | 26 | 133.46 | 16 |
| s298 | 22.17 | 21 | 15.85 | 15 |
| s38417 | 161.73 | 22 | 154.14 | 14 |
| s38584.1 | 149.41 | 22 | 146.03 | 13 |
| seq | 15.03 | 19 | 15.32 | 16 |
| spla | 45.77 | 26 | 42.25 | 18 |
| tseng | 10.09 | 29 | 10 | 19 |
| Geo. | 40.38 | 21.94 | 38.46 (-4.75%) | 14.83 (-32.44%) |

Interestingly, S-Pathfinder reduces the overall runtime (placement & routing) by 4.75% on average. This is due to the fact that S-Pathfinder reduces the number of iterations in routing by 32.44%. Within each iteration, timing analysis is only performed once.

ii) Interaction between placement and routing

| Placement | Deterministic | Stochastic | Deterministic | Stochastic |
| --- | --- | --- | --- | --- |
| Routing | Deterministic | Deterministic | Stochastic | Stochastic |
| Tmean (ns) | 23.43 | 22.65 (-3.3%) | 22.96 (-2.0%) | 22.55 (-3.8%) |
| Tdev (ns) | 3.42 | 3.23 (-5.6%) | 3.35 (-2.1%) | 3.22 (-5.9%) |
| YL (pp10K) | 2.37 | 0.36 | 0.95 | 0.28 |
| Runtime | 1X | 2.86X | 0.95X | 3.10X |