| Single-Vdd | Single-Vdd with power-gating |
| --- | --- |
| EdTLC-NW | Deterministic extended network flow based budgeting for VddP interconnects |
| V-EdTLC-S | Variation aware greedy based assignment |
| V-EdTLC-NW | Variation aware network flow budgeting |

In summary, EdTLC-NW reduces interconnect power by 51.2% but degrades timing yield from 97.7% to 87.5% compared to Single-Vdd. The cut-off delay is set to mean+2*std in Single-Vdd for all cases. V-EdTLC-S and V-EdTLC-NW reduce interconnect power by 40% and 39.5% respectively without degrading timing yield. V-EdTLC-S takes 3.6X runtime compared to V-EdTLC-NW.

Detailed experimental results are presented in the following.

Timing:

|  | Single-Vdd | EdTLC-NW | V-EdTLC-S | V-EdTLC-NW |
| --- | --- | --- | --- | --- |
| circuits | mean | std | cut-off | Yield | mean | std | Yield | mean | std | Yield | mean | std | Yield |
| alu4 | 1.94E-08 | 2.86E-09 | 2.52E-08 | 97.7% | 2.17E-08 | 3.42E-09 | 84.4% | 1.95E-08 | 2.84E-09 | 97.7% | 1.95E-08 | 2.84E-09 | 97.7% |
| apex2 | 2.26E-08 | 3.24E-09 | 2.91E-08 | 97.7% | 2.50E-08 | 3.75E-09 | 86.2% | 2.27E-08 | 3.22E-09 | 97.6% | 2.27E-08 | 3.22E-09 | 97.6% |
| apex4 | 1.93E-08 | 2.52E-09 | 2.44E-08 | 97.7% | 2.11E-08 | 3.10E-09 | 85.4% | 1.93E-08 | 2.53E-09 | 97.7% | 1.93E-08 | 2.53E-09 | 97.7% |
| bigkey | 1.11E-08 | 1.28E-09 | 1.37E-08 | 97.7% | 1.27E-08 | 1.62E-09 | 73.4% | 1.12E-08 | 1.27E-09 | 97.6% | 1.12E-08 | 1.27E-09 | 97.6% |
| clma | 3.96E-08 | 5.21E-09 | 5.00E-08 | 97.7% | 4.39E-08 | 6.42E-09 | 82.8% | 3.95E-08 | 5.22E-09 | 97.8% | 3.96E-08 | 5.22E-09 | 97.7% |
| des | 2.20E-08 | 3.12E-09 | 2.83E-08 | 97.7% | 2.52E-08 | 3.89E-09 | 78.4% | 2.20E-08 | 3.11E-09 | 97.8% | 2.20E-08 | 3.11E-09 | 97.8% |
| diffeq | 2.62E-08 | 5.04E-09 | 3.62E-08 | 97.7% | 2.73E-08 | 4.86E-09 | 96.7% | 2.66E-08 | 4.84E-09 | 97.7% | 2.66E-08 | 4.83E-09 | 97.7% |
| dsip | 1.04E-08 | 1.41E-09 | 1.32E-08 | 97.7% | 1.12E-08 | 1.62E-09 | 88.8% | 1.04E-08 | 1.40E-09 | 97.6% | 1.04E-08 | 1.40E-09 | 97.6% |
| elliptic | 3.05E-08 | 5.08E-09 | 4.07E-08 | 97.7% | 3.22E-08 | 5.33E-09 | 94.5% | 3.09E-08 | 4.88E-09 | 97.8% | 3.09E-08 | 4.92E-09 | 97.7% |
| ex1010 | 2.68E-08 | 3.21E-09 | 3.32E-08 | 97.7% | 2.98E-08 | 4.15E-09 | 79.6% | 2.68E-08 | 3.22E-09 | 97.7% | 2.68E-08 | 3.22E-09 | 97.7% |
| ex5p | 2.00E-08 | 2.67E-09 | 2.54E-08 | 97.7% | 2.17E-08 | 3.15E-09 | 87.8% | 2.00E-08 | 2.68E-09 | 97.8% | 2.00E-08 | 2.68E-09 | 97.8% |
| frisc | 4.18E-08 | 7.54E-09 | 5.68E-08 | 97.7% | 4.34E-08 | 7.52E-09 | 96.3% | 4.19E-08 | 7.48E-09 | 97.7% | 4.19E-08 | 7.48E-09 | 97.7% |
| misex3 | 1.86E-08 | 2.48E-09 | 2.35E-08 | 97.7% | 2.03E-08 | 2.96E-09 | 86.3% | 1.86E-08 | 2.48E-09 | 97.7% | 1.86E-08 | 2.48E-09 | 97.7% |
| pdc | 2.79E-08 | 3.54E-09 | 3.50E-08 | 97.7% | 3.09E-08 | 4.33E-09 | 82.7% | 2.79E-08 | 3.53E-09 | 97.8% | 2.79E-08 | 3.53E-09 | 97.8% |
| s298 | 3.87E-08 | 5.90E-09 | 5.05E-08 | 97.7% | 4.11E-08 | 6.52E-09 | 92.5% | 3.87E-08 | 5.87E-09 | 97.8% | 3.87E-08 | 5.88E-09 | 97.7% |
| s38417 | 3.01E-08 | 4.16E-09 | 3.84E-08 | 97.7% | 3.27E-08 | 4.64E-09 | 89.2% | 3.02E-08 | 4.14E-09 | 97.7% | 3.02E-08 | 4.13E-09 | 97.7% |
| s38584 | 2.09E-08 | 4.04E-09 | 2.90E-08 | 97.7% | 2.28E-08 | 4.01E-09 | 93.9% | 2.16E-08 | 3.68E-09 | 97.8% | 2.16E-08 | 3.71E-09 | 97.7% |
| seq | 1.83E-08 | 2.51E-09 | 2.33E-08 | 97.7% | 2.01E-08 | 2.86E-09 | 87.0% | 1.83E-08 | 2.49E-09 | 97.8% | 1.83E-08 | 2.48E-09 | 97.8% |
| spla | 2.51E-08 | 3.11E-09 | 3.13E-08 | 97.7% | 2.70E-08 | 3.72E-09 | 87.6% | 2.51E-08 | 3.12E-09 | 97.7% | 2.51E-08 | 3.12E-09 | 97.7% |
| tseng | 2.37E-08 | 4.21E-09 | 3.21E-08 | 97.7% | 2.42E-08 | 4.34E-09 | 96.6% | 2.38E-08 | 4.18E-09 | 97.7% | 2.38E-08 | 4.16E-09 | 97.7% |
| avg. |  |  |  | 97.7% |  |  | 87.5% |  |  | 97.7% |  |  | 97.7% |

Power

|  | Single-Vdd |  |  | EdTLC-NW |  |  | V-EdTLC-S |  | V-EdTLC-NW |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Interconnect Power (watt) | Power saving (%) |  | Power saving (%) |  | Power saving (%) |  |
| circuits | dynamic | leakage | total | dynamic | leakage | total | dynamic | leakage | total | dynamic | leakage | total |
| alu4 | 1.17E-02 | 4.20E-04 | 1.21E-02 | 50.4% | 67.8% | 51.0% | 24.8% | 38.5% | 25.3% | 23.0% | 37.3% | 23.5% |
| apex2 | 1.72E-02 | 7.77E-04 | 1.80E-02 | 50.6% | 67.7% | 51.4% | 32.8% | 45.4% | 33.3% | 33.1% | 44.9% | 33.7% |
| apex4 | 8.10E-03 | 5.18E-04 | 8.62E-03 | 46.6% | 61.3% | 47.5% | 26.0% | 27.0% | 26.1% | 24.7% | 27.3% | 24.9% |
| bigkey | 1.77E-02 | 5.40E-04 | 1.82E-02 | 47.5% | 66.0% | 48.1% | 30.6% | 46.3% | 31.1% | 30.9% | 46.9% | 31.4% |
| clma | 3.33E-02 | 5.84E-03 | 3.92E-02 | 50.6% | 67.7% | 53.1% | 46.9% | 56.7% | 48.3% | 46.5% | 57.2% | 48.1% |
| des | 1.95E-02 | 8.33E-04 | 2.03E-02 | 49.8% | 67.2% | 50.5% | 38.0% | 53.7% | 38.6% | 37.6% | 53.8% | 38.3% |
| diffeq | 1.78E-03 | 4.89E-04 | 2.27E-03 | 50.9% | 69.0% | 54.8% | 50.9% | 68.0% | 54.6% | 50.9% | 68.3% | 54.7% |
| dsip | 1.98E-02 | 5.19E-04 | 2.03E-02 | 46.3% | 65.7% | 46.8% | 36.2% | 55.5% | 36.7% | 36.3% | 55.9% | 36.8% |
| elliptic | 4.49E-03 | 1.37E-03 | 5.86E-03 | 50.7% | 68.8% | 55.0% | 50.3% | 67.2% | 54.3% | 50.4% | 67.2% | 54.3% |
| ex1010 | 9.67E-03 | 1.89E-03 | 1.16E-02 | 48.9% | 65.2% | 51.6% | 26.7% | 37.0% | 28.4% | 25.2% | 38.2% | 27.3% |
| ex5p | 4.94E-03 | 4.92E-04 | 5.44E-03 | 47.0% | 63.9% | 48.5% | 31.1% | 40.8% | 32.0% | 32.3% | 42.7% | 33.3% |
| frisc | 3.61E-03 | 2.21E-03 | 5.82E-03 | 51.0% | 68.9% | 57.8% | 50.5% | 68.6% | 57.4% | 50.0% | 68.5% | 57.0% |
| misex3 | 1.23E-02 | 4.88E-04 | 1.28E-02 | 45.7% | 62.4% | 46.4% | 22.1% | 34.6% | 22.5% | 22.5% | 34.8% | 22.9% |
| pdc | 1.98E-02 | 2.70E-03 | 2.25E-02 | 50.1% | 66.9% | 52.1% | 37.1% | 48.6% | 38.5% | 30.0% | 46.7% | 32.0% |
| s298 | 3.21E-03 | 5.99E-04 | 3.81E-03 | 50.1% | 67.4% | 52.8% | 48.7% | 60.5% | 50.6% | 48.8% | 61.2% | 50.7% |
| s38417 | 1.63E-02 | 2.25E-03 | 1.86E-02 | 49.6% | 67.8% | 51.8% | 44.1% | 62.7% | 46.3% | 44.6% | 63.4% | 46.8% |
| s38584 | 1.84E-02 | 1.84E-03 | 2.02E-02 | 50.9% | 68.9% | 52.5% | 51.3% | 68.1% | 52.8% | 50.7% | 68.3% | 52.3% |
| seq | 1.72E-02 | 6.68E-04 | 1.78E-02 | 48.6% | 65.2% | 49.2% | 31.7% | 41.8% | 32.1% | 31.2% | 42.1% | 31.6% |
| spla | 1.62E-02 | 1.65E-03 | 1.78E-02 | 47.6% | 63.7% | 49.1% | 36.0% | 44.1% | 36.7% | 35.4% | 44.1% | 36.2% |
| tseng | 1.94E-03 | 3.63E-04 | 2.30E-03 | 50.8% | 68.6% | 53.6% | 50.7% | 68.0% | 53.4% | 50.7% | 67.8% | 53.4% |
| avg. |  |  |  | 49.2% | 66.5% | 51.2% | 38.3% | 51.7% | 40.0% | 37.7% | 51.8% | 39.5% |

Runtime

| circuits | EdTLC-NW | V-EdTLC-S | V-EdTLC-NW |
| --- | --- | --- | --- |
| alu4 | 44 | 422 | 230 |
| apex2 | 105 | 1363 | 776 |
| apex4 | 39 | 355 | 236 |
| bigkey | 68 | 1679 | 771 |
| clma | 7027 | 166398 | 41726 |
| des | 114 | 1514 | 847 |
| diffeq | 64 | 862 | 27 |
| dsip | 65 | 731 | 147 |
| elliptic | 355 | 7497 | 753 |
| ex1010 | 676 | 7972 | 5838 |
| ex5p | 50 | 263 | 230 |
| frisc | 933 | 14228 | 669 |
| misex3 | 61 | 292 | 344 |
| pdc | 1333 | 14610 | 10133 |
| s298 | 128 | 913 | 336 |
| s38417 | 1200 | 31796 | 4158 |
| s38584 | 835 | 18299 | 396 |
| seq | 102 | 631 | 386 |
| spla | 489 | 4889 | 4375 |
| tseng | 31 | 243 | 19 |
| Geo. | 197 | 2322 | 651 |
| Normalized | 1.00X | 11.82X | 3.31X |

VddL Switch %

| circuits | EdTLC-NW | V-EdTLC-S | V-EdTLC-NW |
| --- | --- | --- | --- |
| alu4 | 97.4% | 58.5% | 57.6% |
| apex2 | 97.7% | 67.4% | 66.9% |
| apex4 | 87.3% | 42.7% | 42.8% |
| bigkey | 95.1% | 68.5% | 68.7% |
| clma | 97.7% | 82.6% | 83.3% |
| des | 97.0% | 75.7% | 75.9% |
| diffeq | 99.1% | 97.4% | 97.8% |
| dsip | 94.8% | 78.9% | 79.7% |
| elliptic | 99.2% | 96.7% | 96.8% |
| ex1010 | 93.6% | 59.1% | 60.6% |
| ex5p | 90.2% | 60.1% | 61.9% |
| frisc | 99.7% | 98.9% | 98.7% |
| misex3 | 89.4% | 53.3% | 53.4% |
| pdc | 96.3% | 73.6% | 72.3% |
| s298 | 96.6% | 87.4% | 87.9% |
| s38417 | 97.9% | 89.9% | 91.2% |
| s38584 | 99.4% | 97.9% | 98.4% |
| seq | 93.6% | 63.0% | 63.6% |
| spla | 91.1% | 65.4% | 65.6% |
| tseng | 98.5% | 97.4% | 97.2% |
| Avg. | 95.6% | 75.7% | 76.0% |