Quick Charging Patents

---
US6154011
Charging of Batteries
Lan T Lam, et. all
- Basic Idea (lead acid batteries)
    - Quickly charge the battery subject to a “gassing” constraint
    - Determine constraint by finding the Resistance Free Maximum Pulsed Voltage (set as an upper limit) such that gassing does not occur
    - Determine the Maximum Pulsed Current such that the above voltage is within limits
    - As charging continues, the Resistance Free Voltage will increase
    - Once the maximum voltage is obtained (upper limit is reached), switch to a charging profile that maintains this voltage
        - i.e., slower charging

---
Different Charging Methods
- Change in amplitude
- Change in Pulse OFF time
- Change in Pulse ON time

---
When to switch charging methods
- Charging Constraints
    - Have both Resistance Free Maximum Pulsed Voltage, AND Resistance Free Average Pulsed Voltage levels
    - If either voltage is reached, we switch charging methods
- Second Stage Charging (IPC-IPC)
    - Once Pulsed Charging Current drops to a certain level, it will take a very long time for charge to be transferred to the battery
    - Therefore, determine a NEW voltage constraint level (may lead to gassing, but is not excessive)
        - New constraint: Maximum, Average, or both
    - Adjust charging current to deliver appreciable charge but also obey the constraint

---
Switching Charging Methods (cont.)
- Second Stage Charging (IPC-IPV)
    - If the current does not deliver appreciable charge, switch to a Pulsed Voltage signal
    - This IPV signal will be one such that the determined Minimum Averaged Pulsed Current delivers appreciable charge
    - In this case, the battery may be discharged (falling edge of IPV signal) which relieves gassing (Fig 7)

---
Stage 2 Charging methods
- Different Constraints
    - Minimum Average Pulsed Current to deliver appreciable charge
    - New Resistance Free Maximum Pulsed Voltage
    - New Resistance Free Average Pulsed Voltage
- 2 Options
    - A new Interactive Pulsed Current to deliver appreciable charge
    - A new Interactive Pulsed Voltage to deliver appreciable charge

---
Battery Apparatus
- Short Version
    - Inputs: Current, Terminal Voltage
    - Output: Power
        - Has a “power stage” to compare output power and required power, thus adjusting current/voltage correspondingly
    - Controlled via micro-controller and closed feedback loop
    - Stores measurement values in host computer (does not specify a cloud, just a network connected host comp)

---
Simulation
- Discharge Simulation
    - Uses SFUDS (Simplified Federal Urban Driving Schedule) = series of constant power steps (fig 9)
- Benefits of this charging method
    - Longer battery life
      - 320 cycles with pulsed charging, 200 cycles with conventional charging
    - Faster Charging (Fig 12)
      - Conventional charge ~ 16 hours
      - ~ 5 minutes to return to 50% charged
      - ~ 11 minutes to return to 80% charged
      - Overcharging to 110% is 60-160 minutes

---
US7339354
Rechargeable Battery Charging Method and Apparatus
Akira Sanpei, et. all
- Basic Idea (Li-Ion battery)
    - Charge at a CC until a specified voltage is reached
    - Begin Pulse Charging until a second voltage is reached
    - Continue Pulse Charging until the terminal voltage does not drop below second voltage
    - When the terminal votlage does not drop below the second voltage 2 or more times, halt charging

---
Algorithm in Detail
- Charging Method
    - Determine a first set voltage V1 (does not say how; must be arbitrary but logical)
    - Constant Current (CC) charging until terminal voltage reaches V1
        - Let An = time that has elapsed since V1 was reached
        - Let Bn = terminal voltage when CC charging is halted
        - Both An and Bn are measured many times
    - Determine if Bn will drop down to a second voltage V2 before An reaches a new time T2
        - T2 is arbitrary, but seems to be a few seconds (e.g., 4s)
        - V2 is also a predetermined amount (not derived)

---
Algorithm in Detail (cont.)
- Charging Method (cont.)
    - If Bn < V2 after a time An > T2, begin pulse charging Bn with ONE pulse (pulse length = T1, arbitrary but ~ 1s in example)
        - If Bn > V2 at time An > T2, skip the next line
    - Continue pulse charging until Bn > V2
    - Calculate Bn at time An=T3 = infinity
        - Equations are included in patent that allow for this calculation of Bn at time T3=infinity
    - If Bn > V2 at time T3 for 2 consecutive calculations, halt charging

---
Algorithm Flowchart
- See Fig 2 in patent
- Additionally, see Fig 6 for a different style flowchart of calculation in the controller circuit

---
US20100156355
System and Method for Charging a Plug-In Electric Vehicle
Paul A. Bauerle, et. all
- Basic Idea
    - Use sensed conditions of the battery to determine a charging signal
    - Battery charger is operated in accordance to this charging signal and sensed conditions
    - Sensing measurements include
      - External: droop voltage, current draw, power loss, power draw, minimum voltage
      - Internal (battery): temperature, voltage, current, SOC, SOH
      - Charger: temperature, charger voltage, charger current
    - Charging Signal Control
      - Compare sensed value to expected value (determine error)
      - Multiply error by a gain
      - Determine new charging signal based on above calculation

---
Charging (cont.)
- Basic Idea (cont.)
    - User interaction with system
      - Setting one of the constraints in charging process
      - Setting the current drawn from ext source (as constraint)
      - Setting the power drawn from ext source (as constraint)
    - Control Methods
      - Setting an overshoot value
      - Using a PID controller to obtain charging signal
      - Using PWM to vary current signal
    - Fault conditions
      - Ability to evaluate if a fault (constraint violation) occurs to stop charging process
      - Setting a diagnostic code to alert the user to such fault

---
Charging (cont.)
- Basic Idea (cont.)
    - External Power Source abilities
      - Uses OCV of this source (not battery) to determine external sensed conditions
    - More information
      - Using the above method for a PHEV plugged into an AC wall socket
      - Outlines the method for using the above method for a PHEV
      - Outlines components needed to perform this “fast charge” for a PHEV

---
US6677730
Device and Method for Pulse Charging a Battery and for Driving other devices with a Pulse
John C. Bedini, et. all
- Note
    - This patent goes into detail about each component of the device (FETs, converters, capacitor banks, etc.) so the details are excluded
- Basic Idea
    - Another type of Pulse Charging Method
    - For the components listed in the patent (with their specified values), pulses last ~100ms with ~250A amplitude

---
Summary of Method
- Pulsed Charging
    - Capacitor bank accumulates charge from an input source (i.e., an AC wall socket) until it reaches a specified level (does not say if it is full or not, but most likely)
    - Capacitor bank is disconnected from input source, thus creating a free-floating energy source
    - Capacitor bank is connected to the battery
    - Capacitor bank pulse charges the battery at a high voltage
    - When empty, capacitor bank reconnects to input source
    - Repeat above process for Pulse Charging

---
Pulsed Charging Method with Cap
- Benefits of using this method
    - Momentary disconnect from charging source gives the battery a “rest period”
      - Perhaps we could sample some useful information during this rest period where it is disconnected
    - Allows for pulse charging
    - Less energy from primary energy source (input source)
      - Not sure how, but they mention it

---
US6954051
Battery Charger and Charging Method
Danh T. Trinh, et. All
- Note
    - This patent gives some background on current charging methods along with a detailed explanation of the battery charger components
    - Details of the actual patent were excluded (not relevant to what we want, just explains how the details works rather than the idea/concept) but the basic ideas are summarized
- Background/Motivation
    - Most charging methods use temperature, voltage, time, or slope as a cutoff for charging, but all are subject to serious issues that may damage the cell

---
Charging Method
- Algorithm (NiCad batteries)
    - For NiCad batteries, a distinct, general form of the VT graph during charging is available
        - The curve is broken into several regions (fig 1.)
        - Although this curve may have some variation due to temp, SOC, etc., there is a clear general form where all parts are identified
    - The curve has specific inflection points (A and B)
        - Inflection points are determined as the second derivative of VT graph (change in sign of slope)
        - Once A is reached, charging switches to a “maintenance” or “topping” mode
        - Once B is reached, we know to stop charging soon (does not specify when, just suggests “middle of region 4”)

---
Charging Method (cont.)
- Algorithm (cont.)
    - Charging is performed via Pulse Charging
        - Specific values are mentioned in the patent's claims in the overview of the main page (10-240 ms pulse length for 2.5A charger, for example)
    - Basically, this patent is a method of determining when to STOP charging
- Issues
    - In a battery pack, one cell may be “sleeping” and when it “wakes up” may lead to a jump in voltage
        - This jump leads to a miscalculated inflection point
    - Damaged batteries do not follow the generalized VT curve

---
US6789174
Method of Terminating Charge for a Battery
James Cornett, et. all
- Background
    - Want to determine conditions for when we stop charging a battery
    - Previous methods use termination voltage
      - When voltage gets to a specified level, stop charging
    - Termination Voltage methods suffer from ionic relaxation
      - Voltage will drop to a steady state
      - Results in less charge than initially thought of from voltage

---
Analogy

---
Charging Method
- Algorithm (3 steps to termination)
    - Begin charging (I believe it is CC charging)
      - The current is constantly monitored and stored
    - Start a timer
    - Measure the Vmax of the battery (for a battery pack, Vmax is Vmax of an individual battery)
    - Compare Vmax to a specified Vthresh
    - Once Vthresh is achieved, stop charging (step 1)
      - Allow a predetermined wait time T_off to elapse so ionic-relaxation occurs
        - This is like pouring in a little root beer and waiting for the head to disappear (essentially, creates pulse charging)

---
Charging Method (cont)
- Algorithm (cont.)
    - Once T_off has elapsed, measure Vmax again
    - Compute the I_avg (from stored current values) and compare to I_min
      - Circuitry keeps a running average of current
    - If I_avg < I_min, it assumes there is an increased impedance and thus a full charge has occurred (step 2)
    - If current falls below I_min, check to see if there is a power source connected
    - If no power source coupled to the battery, there is no need to terminate charging
        - HOW is this possible? You cannot continue to “not terminate charging” if there is no power source to actually charge the battery

---
Charging Method – Special
- Defective Batteries
    - If the Vmax of the battery does not reach Vthresh before the timer runs, we know the battery cannot store any charge and check if there is a defect
    - If timer runs out, stop charging and set an error notification
    - Check to see if Vmax < Vthresh still after disconnect
      - If yes, prevent any charging until error is resolved
      - If no, then there may have been some other error