- All about when to STOP charging a battery

- Previous methods use termination voltage to determine when to stop

    - When the voltage reaches a specified level, the charging current is shut off and we complete charge

    - However, “ionic relaxation” is an issue for this because the voltage will drop significantly until a steady state is achieved

        - resulting in less charge

    - A very, very interesting analogy:

- Charging method

    - Begin charging (does not specify CC, CV, or Pulse, but I think it is CC)

        - The current is constantly monitored and stored

    - Start a timer

    - Measure the Vmax of the battery (Vmax of any 1 cell)

    - Compare Vmax to Vthresh

    - Once Vthresh is reached, stop charging

        - Allow a predetermined wait time (T_off) to elapse so ionic-relaxation occurs

        - This is like pouring in a little root beer and waiting for the head to disappear (similar to pulse charging)

    - Once T_off has elapsed, measure Vmax again

    - Compute the I_avg (from all charging current values) and compare with I_min

        - The circuitry keeps a running average of the current

        - If it falls below I_min, it assumes it is due to an increased impedance and thus a full charge

    - If current falls below I_min, check to see if there is a power source connected

    - *If there is no power source coupled to the battery, there is no need to terminate charging

        - HOW is this possible? How can you “not terminate charging” when you can't charge to begin with since there is no power source?!?!?!

- Defective batteries

    - If the Vmax of the battery does not reach Vthresh before the timer runs out, we know the battery cannot store charge and there is a defect

    - If timer runs out, stop charging and set an error notification

    - Check to see if Vmax < Vthresh still holds

        - If yes, prevent any charging until error is resolved