Typical I/O standards for general purpose

| I/O Standard | Application | Voltage | Drive Current (mA)1 | Performance (MHZ) |
| --- | --- | --- | --- | --- |
| LVTTL (Low Voltage Transistor-Transistor Logic) | General Purpose | 3.3v | 24, 16, 12, 8, 4 | 350 |
|  |  | 2.5v | 16, 12, 8, 2 | 350 |
|  |  | 1.8v | 12, 8, 2 | 250 |
| LVCMOS (Low Voltage CMOS) | General Purpose | 3.3v | 24, 12, 8, 4, 2 | 350 |
|  |  | 2.5v | 16, 12, 8, 2 | 350 |
|  |  | 1.8v | 12, 8, 2 | 250 |
|  |  | 1.5v | 8, 4, 2 | 225 |

- Programmable Output Drive Current may differ from Altera to Xilinx FPGA chip. Here shows the Altera Stratix spec.

Diagram of IOB from Xilinx Spartan-3

Input Delay Circuit from Xilinx Spartan-3

Keeper Circuit from Xilinx Spartan-3