Weekly report Jan. 14th 2004

In this week, I analyzed power breakdown of trace-base power estimator. The average error compared to the cycle accurate estimator is shown in the following table.

|  | ave_error % | max_error % | % of total power(regular setting) |
| --- | --- | --- | --- |
| logic static | 5.75 | 10.7 | 11.49917531 |
| logic_dynamic | 72 | 78 | 0.328673126 |
| logic | 7.1 | 16 | 11.8278484 |
| global static | 3.3 | 8.7 | 49.98017911 |
| global_dynamic | 24 | 35 | 4.413353283 |
| global | 0.4 | 1.2 | 54.3935137 |
| local static | 0.1 | 1.1 | 31.41553706 |
| local_dyanmic | 21 | 35 | 2.186729338 |
| local | 0 | 0 | 33.60227227 |

The estimator error is mainly from interconnect dynamic power. The local interconnect dynamic power was over estimated and the global interconnect dynamic power is under estimated. The coming work is to check the power estimator to figure out the reason. To my opinion, the main reason is the short circuit power ratio. Therefore, I am going to fix the short circuit power ratio to improve the power estimator.

Moreover, I also compare the power breakdown for the best hype-arch which is (12, 4) with heterogeneous Vt and power gating. In such architecture, the % of dynamic power increases. The dynamic power is about 35% of the total power, as shown in the following table. Here the dynamic power become significant, especially the global dynamic power.

|  | %of total power (best hype-arch) |
| --- | --- |
| logic static | 7.294229193 |
| logic_dynamic | 1.328207321 |
| logic | 8.622437296 |
| global static | 38.85435929 |
| global_dynamic | 18.79570368 |
| global | 57.65002049 |
| local static | 22.93510904 |
| local_dyanmic | 9.323840039 |
| local | 32.25894214 |