FPGA Leakage Modeling Considering Process Variations

Week 10 Progress Report 3/21/05

Wong, Ho-Yan Phoebe

Currently working on setting up HSPICE simulation with process variations on Leff, Tox, and Vt.

- Research on the commonly used variability numbers for the above 3 variations. Related paper include: S. R. Nassif, “Modeling and Forecasting of Manufacturing Variations”, DAC 2000.

In the paper, the following 3-sigma variation ranges are given for 70nm technology:

| Leff | 33.0 nm |
| --- | --- |
| Tox | 0.48 nm |
| Vt | 40.0 mV |

After verifying the above variability numbers can be adopted, then HSPICE simulations will be done in the +/- 3 sigma range.