Weekly report Jan 21st 2005

Lerong Cheng

In this week, I do the following two research jobs:

- Improve the accuracy of the Trace-base estimator. The error of dynamic power is still large. The main reason is the short circuit power ratio. I try to use different short circuit for different circuit instead of using uniform ratio for all circuits. This programming and data correcting is in progress.

- Design keeper to reduce the interconnect leakage power. In the interconnect, because the voltage degradation after a mux (built with pass transistor), the sub-threshold leakage of the buffer is much larger. There are two ways to compensate this effect, one is gate boosting and the other is applying keeper in the buffer. I am now running spice to find out the best size for the keeper transistor.

On going work.

In the coming week, I plan to finish the above two jobs.