FPGA Temperature Dependent Leakage Modeling

Week 4 Progress Report 2/4/05

Wong, Ho-Yan Phoebe

1.	Currently experimenting on the “check temperature convergence” function.

Parameters:

Thermal resistance, θaj, of 16.8oC/W (taken from Altera’s Stratix EP1S10),

Unit thermal resistance= θaj * chip area

Ambient temperature of 40oC.

Equation: Tj=Ta+ θaj

Stopping condition:

If the difference between Tj of 2 consecutive cycles < 0.001, temperature converges. Otherwise, indicates thermal runaway.

Preliminary results (still in progress):

At Vdd=1.1, Vt=0.2, find each benchmark’s leakage at the converged temperature.