Lerong Cheng Weekly Report

2/7/2005

In this week, I debugged the code corrected the area estimation. In the previous program, the area overhead coursed by power gating was over estimated.

Table 1 illustrates the delay and area overhead percentage for the min-ED hyper-architecture (vdd=0.9, block-vt=0.3, interconnect-vt=0.25, N=12, K=4) for Class4 (heterogeneous-vt with power gating). In the table, we find that gating transistor size 7 will provide the best area-delay tradeoff.

Table 2 illustrates the delay and area overhead percentage for the min-ED hyper-architecture (vdd=0.9, vt=0.25, N=6, K=7) for Class3 (homogeneous-vt with power gating). We find that gating transistor size 7 will also provide the best area-delay tradeoff. However, in this case, the delay overhead and area overhead is much smaller than class4. This is because such hype-arch has larger LUT size, it needs smaller global interconnect size, therefore, the area overhead introduced by global interconnect gating transistors is smaller.

Table 1

| Gating transistor size | 2 | 4 | 7 | 10 |
| --- | --- | --- | --- | --- |
| delay overhead percentage | 19.75 | 11.76 | 7.79 | 6.28 |
| area overhead ratio | 18.1998 | 23.0932 | 29.4259 | 34.7951 |

Figure 1

Table 2

| Gating transistor size | 2 | 4 | 7 | 10 |
| --- | --- | --- | --- | --- |
| delay overhead percentage | 14.52 | 8.24 | 2.49 | 1.49 |
| area overhead percentage | 10.99 | 13.75 | 17.59 | 21.11 |

Figure 2

On going work:

- Update the experimental result and write the final version for the sDAC submission.

- Write the journal paper of device architecture co-optimization.