FPGA Temperature Dependent Leakage Modeling

Week 5 Progress Report 2/12/05

Wong, Ho-Yan Phoebe

- Implemented the thermal power calculation. Instead of calculating power for each benchmark, now all benchmarks are calculated together as mapped on the same chip.

Parameters:

Thermal resistance, θaj, of 10.6oC/W (taken from Altera’s Stratix EP1S10),

Ambient temperature of 40oC.

Equation: Tj=Ta+ θaj

Stopping condition:

If the difference between Tj of 2 consecutive cycles < 0.001, temperature converges. Otherwise, indicates thermal runaway.

Results:

For θaj, of 10.6oC/W and below, temperature converges. More experiments will be done later.