FPGA Temperature Dependent Leakage Modeling

Week 9 Progress Report 3/13/05

Wong, Ho-Yan Phoebe

Introduction

Based on [1], leakage on FPGA will be modeled considering process variations on channel length, doping concentration, and oxide thickness. Below are the proposed stages:

- Circuit level simulation

Simulate leakage current dependence on channel length, threshold voltage (doping concentration), and oxide thickness using HSPICE. Simulations will be done on buffers, LUTs, DFFs, and SRAM.

- Curve fitting on simulation data

Using the HSPICE data, curve fit each function in the following form:

f(ΔLeff)=-(L+ c 2L2)/c1, 	f(ΔVth)=-(c3/c1)*V, 	f(ΔTox)= -(T/β)

such that 	Ileak=Inominal*f(ΔP)

There is still uncertainties on how to obtain the variability numbers for ΔLeff, ΔVth , and ΔTox. The original paper get the numbers from “an industrial 90nm process”.

- Device level

After getting the above fitted parameters and variability numbers, then the leakage model considering within-die variations could be incorporated into the FPGA power estimator using the following equations:

Ic, tot = Σ Wd [( SL.SV/k)*ILg,Vg+ST*ITg]

- Yield

Since channel length contributed significantly to delay variations, die-to-die channel length variation is considered. The chips that have leakage power exceeding the imposed power limit would be discarded. Same for the chips that have a delay exceeding the delay constraint (e.g. +1 sigma channel length).

References:

- Rajeev Rao, Anirudh Devgan, “Parametric Yield Estimation Considering Leakage Variability”, DAC 2004.

- Rajeev Rao, “Statistical Estimation of Leakage Current Considering Inter-and Intra-Die Process Variation”.