# Weekly Report 09212007

# Zhen Cao

## Paper Reading

- Detail reading on “H.264 Overview”

Get a deeper understanding about techniques in H.264, some important points:

  - Hierarchy of NAL unit steam -> coded video sequences. -> access Unit:

NAL unit steam contains one or more coded video sequences, coded video sequence contains one or more access units. Access unit contains a coded picture. Pictures in one coded video sequences can be decoded independently of other coded video sequences and using only one sequence parameter set.

  - For both intra/inter prediction, prediction across slice boundaries is not used.

  - Both P and B frames can refer to past and future multi-frames, the difference is B frames can refer to two lists of frames of different weight.

- Detail reading on “A Queuing Theoretic Approach to Processor Power Adaptation for Video Decoding System”.

  - The top level problem solved by this paper is: given decoding jobs, with DVS system, to minimize the total energy while keep the video quality.

  - A detail formulation of the top level problem is, using a simple queue model, which allows job done by class sequence (by sequence as GOP1:1,2,…I,GOP2:1,2…), assume the queue is never empty and no static power, find voltage level k for each job, such that minimize the total energy.

  - Problem B can be decomposed to two sub problem: C1, find voltage level k for each job such that the possibility for it to be missed will be less then a given parameter; C2, how to dynamically adapt voltage scaling consider the finish time of last job.

  - For C1, the paper present that the complexity of each job can be decomposed to a few general distribution. Then the serve time and waiting time distribution of each job can be modeled. Then the possibility of one job to miss a given time line T can be calculated.

  - For C2, a simple algorithm that adjusts the just next job finish time line is given.

  - For quality aware problem, with the sorting property of encoding method, the problem can be modeled.

## Working plan:

Aiming at DAC (deadline 19th Nov.), working on multi-function/core dynamic voltage scaling, considering leakage power. Work on the algorithm and software simulation side:

- First get familiar with GEMS.

- Try to add leakage power.

- Try to improve scheduling algorithm.

The modeling part can be helped by student of Mihaela, and the hardware implementation part will be handled by David.