In this week I completed the following work.

- M202 course project

- M209 course presentation, read two papers about technology mapping and prepared slides.

- For FPGA retiming vdd assignment part, to solve the problem that some of the FF assignments are not available (due to the data structure constraint in VPR). I paid the following efforts:

  - I tried to move these FFs to the available FF slot. The following 4 kinds of timing edges are considered in the FF movement after retiming.

For each of these four cases, I moved the FF into its nearest empty slot. After moving FF, I re-construct the timing graph and found that the clock period is much lesser, which indicates that the FF# in the critical path is changed and the functionality of the circuit is changed. Then, I realized that in some cases, we can not even move a FF neither forward or backward. Consider the following case:

If we move FF forward (to edge DE/DF) or backward (to edge AC/BC), the FF# in a certain path will change. Actually, these scenarios exist extensively in my retimed results, which makes it prohibitive to solve the unavailable FF slot problem by moving FF.

  - After realizing the failure of the FF movement, I found that it is hard to accomplish a successful retiming by simply solving a LP formulation and then performing FF assignment in a highly constrained data structure in the current VPR. I tried to add an extra non-linear constraint

(x_v-P)(x_u-P)>=0, for edge (u, v) contains no FF slots      (1)

where P is the clock period, and x_v is the arrival time in timing node v. As all x_v < 2*P by the timing constraint, we can enforce that ceil(x_v)=ceil(x_u) for edge (u, v) contains no FF slots by (1), which make sure that no FF are inserted in unavailable timing edges.

To solve such a quadratic optimization problem, I used an optimization package “Mosek”, which is also used by Yan to solve power-timing-yield robust LP problem. After spending some time learning the usage of Mosek, I used it to solve my quadratic programming problem. But the solver reported the status of the solution of the problem was unknown, which means the results might be unreasonable. I think the reason why Mosek failed to solve this quadratic optimization problem is that the solution space of this problem is not convex. Actually, even the solution space of (x1-P)*(x2-P)>=0 is not convex.

To verify the correctness of my usage of Mosek, I used it to solve the mixed-wire length FPGA vdd assignment problem, I tested a relative larger circuit “frisc”. It took 30 seconds for Mosek to get the solution. Note that “lp_solver” will use more than 20 minutes to solve this problem on the same machine and “network flow” will use about 2-5 seconds. From this experiment, we can find that “network flow” reduces its speedup ratio when we employ interior point method to solve the LP problem.

My conclusion: After these tries, I think that it’s hard to get a feasible FF assignment with a continuous formulation for retiming due to the limitation of available FF slots in VPR. We should try some discrete formulation of this problem as the FF# constraint in certain edges can be easily represented in discrete formulation (without things like ceiling). Hence, I’m going to try the following formulation (similar way used in [N. Chabini, GLSVLSI’03] for voltage scaling) in the next week.

Forumla-1 (original version from C.E. Leiserson, algorithmica’91, I modified it for delay associated in edges instead of nodes)

Ojb: the same as my last formulation

Constraint:

- –s(v) <= -d(u, v), for all timing node v in edge (u,v)

- s(v) <= P, for all timing node v

- r(u) – r(v) <= FF(u,v), for all edge (u,v)

- s(u) – s(v)<=-d(u,v), for all edge (u,v) and r(u) – r(v)=FF(u,v)

In fact, this formulation intends to find a set of retiming values r(v) and a set of arrival times s(u) simultaneously.

If we do the following substitution:

Let R(v) = r(v)+s(v)/P

Then formula-1 can be re-written as:

Forumla-2 (original version from C.E. Leiserson, algorithmica’91, I modified it for delay associated in edges instead of nodes)

Ojb: obj2

Constraint:

- r(v) – R(v) <= -d(u, v)/P, for all timing node v in edge (u,v)

- R(v) – r(v) <= 1, for all timing node v

- r(u) – r(v) <= FF(u,v), for all edge (u,v)

- R(u) – R(v)<= FF(u,v) -d(u,v)/P, for all edge (u,v)

Note that Formula-2 is a MIP and the slack in edge (u, v) can be expressed as

slack(u,v) = s(v) – s(u) – d(u,v) = P(R(v) – R(u) - r(v) + r(u)) + d(u,v), hence,

obj2 = \sum delta_Pwr*slack(u,v)

Additionally, FF# constraints should be added to make sure that all FFs are assigned to available slots:

- r(u) – r(v) =0, for all edges containing no FF slots.

This formulation is more controllable as we explicitly consider retiming values r(v), which is discrete variables in it. Due to the time limitation, I haven’t got result of this formulation. I’ll do it in the next week.