Retiming based timing analysis has been proposed in [1] in the deterministic scenario. The concepts of sequential arrival time (SAT) and sequential required time (SRT) are presented. A Bellman-Ford based algorithm (RTA) is proposed to test the feasibility of a given clock period and calculates the retiming values in the same time if such a clock period is feasible. However, the proposed approach in [1] is hardly extended to handle variations as the operations (ceiling and dividing) used in RTA are not easily performed in statistical way. [2] addresses on statistical performance-driven retiming problem in a general framework. This work employs the statistical timing analysis proposed in [3] and calculates the timing on the combinational paths in retiming process. No retiming based sequential timing analysis is performed in this paper, and no other VLS design processes (e.g placement, routing, etc.) are combined in the proposed retiming framework.

We propose the problem of simultaneous retiming and placement considering process variations which includes two folds, i) retiming based statistical static timing analysis (RSSTA) and ii) timing-driven placement. Using the simulated annealing based placement engine, the cost function in each move is obtained based on the RSSTA results. After each pass of move in SA, we perform RSSTA and get sequential arrival time and sequential required time for each timing node, from which we can get slack of each timing node. Weighting more in critical timing node who has smaller slack, the next moves of SA can be expected to improve the timing of the circuit. Note that retiming values are calculated in the same time efficiently when we perform RSSTA, we actually perform retiming and placement simultaneously.

[1] Jason Cong and Sung Kyu Lim, "Retiming-Based Timing Analysis with an Application to Mincut-Based Global Placement", TCAD'04

[2] Jia Wang and Hai Zhou, Minimal Period Retiming Under Process Variations, GLSVLSI'04

[3] H. Chang and S. Sapatnekar, "Statistical timing analysis considering spatial correlations using a single pert-like traversal", ICCAD, 2003