Report of the EDA Roadmap Taskforce

on the Design of Microprocessors

DRAFT 2

INTRODUCTION

This Roadmap is first in a series that attempts to project the future of technology.  It is built on the National Technology Roadmap for Semiconductors 97.  This Roadmap is sponsored by the EDA (Electronic Design Automation) Industry Council.  The Industry Council is a committee that comprises EDA suppliers including EDAC, EDA users from both system companies, and semiconductor companies, as well as industry organizations including Sematech, SRC, and Si2.  This Taskforce was funded by DARPA and the work was administrated by Si2.

The EDA Industry Council chartered the EDA Roadmap Taskforce to select one electronic marketplace and examine what changes are required to design effectively five years hence.  Implied by the Industry Council, is the worry that the industry is unprepared for the future.  Their hope is that an early prediction of needs and capabilities would allow enough lead-time for the development of the required advancements.

The EDA Roadmap Taskforce first met in February, 1998.  The Taskforce is comprised of 31 experts with processing, design, or EDA backgrounds.  They include representatives from both vendors and consumers of EDA*.  Many of the participants have a history in more than one of these fields.  We examined several target markets and chose High-end Microprocessor design as the most challenging.  We expected that other taskforces will concentrate on such markets as telecom, PCs, consumer electronics, etc.  We also targeted designs that will begin in 2003, the time frame sets that semiconductor processes to be smaller than one hundred nanometers.

Figure 0.1 Process:   Focus on Change

The EDA Roadmap Taskforce met six times during 1998.  It began by investigating where paradigm shifts will occur.   This included forecasting directions of the semiconductor processing, design approaches, and electronic design automation.

Figure 0.2 Technology Trends

The semiconductor process information is extracted from the SIA National Technology Roadmap for Semiconductors '97 (NTRS97).  The EDA information includes extrapolations from public plans that are published by commercial EDA companies.  Much of the design information that the Taskforce obtained is anecdotal and it is not publishable.  All anecdotal data was verified by determining if similar sources gave equivalent responses.  In fact, the “stories” are surprisingly similar. The forecasts presumed that each technology will be enhanced in intervening years.  The Taskforce wants to build on these enhancements and to emphasize other aspects where technology must be reshaped, or created.

Next, the Taskforce examined alternative solutions for the paradigm shifts.   The solutions included modification of semiconductor processing, changing design methodology, and creating new EDA tools. We concluded that each of these arenas, required changes or modifications to meet the challenges of the future.  We also concluded that additional research is required in a number of areas.

Figure 0.3 Design Pushing Frequency through Architecture and Circuit Changes

Some of the changes directly impact design.  For example, small geometries make high speed circuits possible.  Other changes have an indirect impact.  For example, many transistors operating at high speed, even at reduced voltages, will consume great amounts of power.

Figure 0.4  Power Rises Sharply

This Taskforce Report is organized around technology driven paradigm shifts and solutions to these paradigm shifts.

Section 1  Target Design

Section 2  Power

Section 3  Signal Integrity and Delay Variation

Section 4  Design Productivity

Section 5  Test

Section 6  EDA System Structure

Section 7  Conclusions

Section 8  Further Research Needed.

*Members of the EDA Roadmap Taskforce.  Each member’s affiliation indicates their association at time that the member joined the committee.  The Taskforce was comprised of highly experienced technologists.   They strove to advance our science.

Paul Weil, Co-Chair, Intel

Arny Goldfein, Co-Chair, Cadence

Shakhar Borkar, Intel

Pat Capapano, Motorola

Jason Cong, UCLA

Don Cottrell, Si2

Carlos Dangelo, LSILogic

Steve Grout, Sematech

Bill Joyner, SRC

Andrew B. Kahng,  UCLA

Sani Nassif, IBM

Rich Newton, UCB

Bryan Preas, Xerox

Steve Sapiro, Consultant

Chuck Shaw, Cadence

Peter Suaris, Mentor

*The Taskforce included the assistance from many other individuals.  We would like to recognize the following for their special contributions to this effort.

Andy Charnas, Sun

John Cohn IBM

Mark Birmbaum, Fujitsu

Phil Fisher, Semitech

Mark Flomenhoft, Intel

Randy Harr, Synopsys

Bernd Koenemann LogicVision

Bob Lashley, Sun

Farad Najm, Univ of Ill

Phil Nigh IBM

Hillel Ofek, Dynalogic

Saila Ponnapalli, IBM

Larry Rosenberg,VSI

Naresh Sehgal,  Intel

Dick Smith, Cadence

Rob Smith, Actel

Ron Walther IBM

Tak Young, Synopsys

SECTION 1

Target Design

Year 2003 - Microprocessor Data Sheet

The Taskforce felt that it was important to identify a typical design that would allow us to evaluate difficulties and select between alternative solutions.  We wanted a target design that represents High End Microprocessors.   These microprocessors will be used as server type computers, to perform mathematical and data operations, and to perform multimedia and speech analysis / synthesis functions.

The Taskforce extrapolated the chip information available in NTRS97, selecting information for microprocessors that begin design in the 2003 timeframe.  The Taskforce expects that these chips will be comprised of 200 Million transistors of which at least 50 Million transistors will constitute logic gates. The chip will be fabricated in a CMOS semiconductor process with 100 nanometer or smaller minimum geometry design rules.  The overall size of the chip will exceed 500 square millimeters. The chips will be encapsulated in packages that have four thousand pins where over half of the pins will be used for power and ground.  The chips will run at high frequencies with basic clock frequencies above 3.5 GHz and with very fast slew rate requiring frequencies above 100 GHz.

Figure 1.1 Target Chip Data Sheet

In summary, .2 Billion transistors where transistors will be switching at microwave frequencies could be a challenge.  In fact, it could be multiple challenges: Large, Small, and High.

·	Large: With .2 Billion transistors to design, while presuming that a designer, with present automation can design 1000 transistors in a day, it will take approximately 500 person-years to create the chip.   The Taskforce identified designer productivity as an very important area to investigate.

·	Small: 1000 Angstroms (100nm) is a shorter wavelength than visible light.  Our process assumptions have changed and many of our design assumptions are changing also. Design is accomplished with a series of simplifications. Heretofore second-order effects will become dominant effects and the simplifications will change.  The Taskforce identified the effect for small geometry effects as one of the changes that need to be investigated.

·	High: The microprocessor clock frequency of 3.5GHz is in the microwave range.  If this signal has sharp edges as one would suspect then the odd harmonics will be required to maintain the waveform shape.  From a Fourier transform standpoint, the third harmonic is 9GHz and if the slew rates are faster then frequencies as high as 100GHz will be important.  At these frequencies, any interconnection approximately 1millimeter long will need to be designed through non-traditional means. The Taskforce identified interconnect as an important area to investigate.

Figure 1.2 Global and Local Interconnect Delays vs. Gate Delays

The Taskforce objective is to find approaches to design larger chips with fewer engineers while being concerned about more detail.  This report identifies enhancements and modifications to semiconductor processing, design methodology and electronic design automation that the Taskforce feels is necessary to reach this objective.

Figure 1.3 Taskforce Objective

SECTION 2

Power

The Taskforce examined the power requirements of processors that will be designed in 2003.  Microprocessors are rated on their speed and design’s highest priority is maximization of processor speed.  To optimize speed, other constraints need to be relaxed.  One design constraint that can be adjusted is power.  Microprocessor designers conveyed that, in the future, microprocessors will consume 100s of watts per chip.  There are a number of mechanisms of removing the heat.  But thermal gradients and high currents are of major concerns.

A simplified approach to examine power (P) is to consider it as a function of capacitance (C), frequency (f), and the power supply voltage (Vdd).  The total capacitance ©  is composed of active and interconnect components that are being charged/discharged between the logic “zero” and “one” levels. As a technology scales down, we acquire more capacitance per unit area since the gate oxide thickness is decreased, and the horizontal wire spacing is reduced.

Figure 2.1 Growth in Active Capacitance

With smaller channel lengths, however, transistor drive increases and results in a net increase in the clock frequency (f). Combined with a general trend to larger chips (and therefore yet more capacitance) these two phenomena overcome the gradual reduction in Vdd and result in a net increase in power dissipation as technology is scaled.

Figure 2.2 More Supply Current

A rule of thumb for estimating power consumed by a digital circuit is:

P = K C f Vdd^2

Where K is a proportionality constant, which accounts for nodes not switching at every clock cycle. However, to achieve ever-higher performance, circuit families (e.g. dynamic/domino CMOS) are being used which have a higher constant K than classic static CMOS.

Chips dissipating 100 to 150 W are currently being designed, and power dissipations of 300 W are anticipated ( we have heard predictions of chips requiring 1000 W discussed.)  This represents a dramatic increase in power. Further, the supply voltage is expected to be approximately 1 volt, the current will increase faster than the power.  We should expect average current greater than 300 amps and transient current double that value for one nanosecond.

Figure 2.3 Power / Voltage = Current

The major challenge is maintaining a near constant supply voltage when delivering - on the average - hundreds of amps with a variation in supply current of hundreds of amps.

With lower supply voltages, the threshold voltage  (Vt) of MOSFETs is scaled down in order to maintain performance. Most often this is accomplished by maintaining Vt  as a fixed proportion of Vdd. Because the sub-threshold current is an exponential function of Vt, this reduction results in a very rapid increase in leakage currents. This leakage current acts to increase the background power dissipation and is very important for low power design.

With higher power supply currents and increased frequencies, the current change (dI/dt)  term increases, while the resistance in the power network is reduced in order to keep rail droop under control. This effectively lowers the threshold at which the dynamic voltage drop (L dI/dt) is comparable to the static drop (R).  This means that rail inductance becomes more important for power supply and noise performance. Even small mutual inductances between power grid and signal interconnect will disrupt signals because of the large dI/dt.

Since power is not expended uniformly throughout the chip, different areas of the chip will experience different temperatures, resulting in thermal gradients across the chip. These gradients result in timing variability (hot circuits are slower) and can lower overall design performance in order to compensate for the extra timing tolerance.

There is significant interaction between the power design, clock design and other global controls.  For most microprocessors, the clock network is probably the largest single consumer of power.  The clock runs at full speed over the longest wires thus requiring appropriate ground return path design in order to keep inductance in check.

Due to excessive power, large chips will turn off portions of the chip.  However, awakening large portions of a chip causes other power surges. Power surges are expected in common situations such as power up and reset.  These are all dramatic effects that will require modifications in processing, design methodology, and in design automation.

The need to keep electrical noise down, demands that the clock network be appropriately shielded with "quiet" power supply wires in order to insulate this circuitry.  The Taskforce recommends that additional layers of metal be used for shielding as well as power and ground plains.  In order to reduce power supply droop, it will be necessary to employ on-chip decoupling capacitance.  Perhaps, we may need to develop a flip-chip technology where there are thousands of power and ground pads each having a decoupling capacitance integrated into the package.

Early in the design cycle, tools are needed to accurately estimate power dissipation for these very large microprocessors.  The early prediction needs to estimate power dissipation, and thermal behavior, current requirements for different areas of a chip. Power planning tools must be fully aware of the current distribution and current dissipation of underlying technology.  That entails knowledge of wire resistance, capacitance, cross capacitance, mutual- inductance and self-inductance parameters, and layout physical design rules. The prediction must anticipate layout issues such as blockages i.e. portions of the chip where the power grid may be only partial.

In order to reduce the power surges that occur at clock edges, it may be important to adopt self timed and asynchronous design techniques for major portions of the chip designs. Some designs, which are entirely asynchronous are already reaching the market (although not at the high end).  Current design tools do not adequately synthesize or analyze self timed and asynchronous designs.  We may need to invent a new category of design automation.

Figure 2.4 Increased Power / Current: Taskforce Recommendations

SECTION 3

Signal Integrity and Delay Variation

Microprocessors are designed for high-speed operation.  The Taskforce investigated factors that limit speeds (GHz) in microprocessors that will be fabricated in CMOS processes with 100nm minimum geometries.  Much of the data that has been used is from the NTRS97 but the data has been enhanced from other sources.

Figure 3.1 Gate / Interconnect Delay

The gate delay noted in the figure above is with no load.  The effect of interconnect delay ranges from negligible to dominant.  For short distances such as within a cell interconnect delay and signal distortion will be negligible.   For the interconnection between major elements of a chip, the effect of interconnect on delay will dominate over other delay characteristics.

Figure 3.2 Delay and Signal Integrity Data

At GHz frequencies, logic signals will not be digital waveforms with slew rates.   They will be similar to analog signals that cross switching points.  These signals will be distorted through interaction with other signals.  This will upset the signal’s integrity and alter the time that the signal will take to reach a  switching point.  This variable time will manifest itself as variable “delay” time.

Physical phenomena that were heretofore ignored will become predominant.  Most notable among these will be self-inductance (particularly in the wide global interconnections), mutual capacitance, and mutual inductance.  Mutual capacitance will be noticeable in higher impedance circuits with low current nets and self and mutual inductance will be dominant in high current nets and especially high di/dt nets.  Each will cause the signal’s integrity to be diminished.

The mutual capacitance and mutual inductance will couple one signal to another.  The couplings will be proportional to the relative slew rates of the two signals, so that the amount of coupling will vary.  The effect of this will be to make signals transition before, during, or after the time they need to switch.  Pre-charged networks may present incorrect information to the following stage switches.  Waveform glitches may impact delay even more significantly if they occur at the switching point where it can cause an actual change of state.

We have examined long word-length microprocessor architectures with multi-clocks.  These synchronous microprocessors switch many nets simultaneously.  The advantage of long word architectures is that many parallel operations can be accomplished concurrently.   However, this leads to multiple signal integrity problems.  In many cases, combinations of mutual capacitors and inductors will effect many signals.

A simple pair of interconnects is used to illustrate the mutual interference problems. One signal is considered of primary interest.  The primary signal’s response is effected by another signal, which is an aggressor.  If a primary signal and aggressor transition close to the same time, then the timing of both signals will be modified from nominal.   For example, if both signals transition at the same time with the same polarity, then there is no change in charge across the mutual capacitance between them. The signal will change faster on both the primary and aggressor nets.  If the signals are opposite in polarity then the mutual capacitance will require double the normal charge and lengthen the delay.

During multiple signal transitions, some signals will rise faster and some slower.  Additionally, the signals will be seriously distorted.  Because 100nm geometry transistors are low gain, some of these distortions will be transmitted to subsequent stages.  These stages will have other aggressors that add other distortions.

The manifestation of distortion in a digital system is delay variation.  Even pre-charging a net will result in delay variation.  Each of these distorted signals will reach their final value if given enough time.  However, in high-speed designs, precautions will need to be taken to assure that the variations will not cause a system malfunction.

Figure 3.3 Delay Variation

Interconnections of approximately 1000nm (10x minimum geometry) may remain unaffected by other signals.  For interconnections that are approximately 100u in length (1000x minimum geometry), the effects of o0ther signals will limit performance and precautions will be needed. Interconnects at the chip level like buses, clocks, reset, and power distribution, must be designed to control the effects of mutual signal distortion.

At some point, buffers will be added to reach a practical maximum delay per mm.  However, when using buffers/inverters, time of flight increases.  Inverter insertion will be most effective if they are inserted in a physically staggered pattern.  The staggering will have the effect of balancing the aggressor signals by inverting the aggressor’s polarity.  This will limit the effect of some challenging situations while it does not help other situations like power distribution and low skew clocks.  The primary benefit of adding buffering is reshaping the signal.  Therefore, the use of  Schmidt Triggers or similar circuit with hysteresis may be more effective in minimizing the impact of delay variations.

Designers will also need to consider the use of shielding to limit the effects of long parallel interconnections or high current.  The effects of running signals over functional blocks will often induce undesirable effects on the block’s timing.  Shielding will greatly reduce signal interference.

Delay uncertainty will be a function of the direct and indirect relationships between signals.  If multiple signals are always spaced temporally, then their mutual effect will be diminished.  If these signals often switch at the same time, and at random polarities then many will impair the timing of the others.

Figure 3.4 Signal Interrelationships

Microprocessors are synchronous and many signals transition concurrently.  To avert problems, designers and / or tools need to look for long runs of parallel wires and analyze them for coupling problems.

There are several essential EDA technologies.  One such technology will be extraction of mutual inductance and capacitance as well as other parameters that effect delay.  Because signal integrity must capture relationships between the signals, delay models will be multi-port.  As we will see, parameter and temperature variations across a chip will also contribute significantly to changes in delays.  Therefore, additional ports will be needed for these variables.  These models will be evaluated in a multi-path logic analysis engine. This multi-path analyzer will need to carry the relationships between signals so that mutual relations will be properly modeled.

The Taskforce recommends that the multi-path logic analysis engine be built into physical design.  Physical design must be signal integrity aware and avoid timing problems whenever possible.  These will include buffering, shielding, variable width interconnections, and interlacing quiet signal lines next to active signal lines.

The Taskforce recommends that physical design be completed in hierarchical stages and that longer more challenging connections be completed before less challenging details.  The Taskforce suggests physical design must be interconnect centric. The higher levels of physical hierarchy with power delivery, global signals such as clocks, and busses and signals between blocks will be designed first.  During the design of the chip level, the lower level functions will be specified and budget set for functional delays. Functional design at the high level will control signal integrity by minimizing the number of signal transitions that implicitly interfere.  Thereby, lower levels of hierarchy will be designed aware of chip level signals that will dominate delay.   This lower level of physical design will concentrate on achieving the delay budgets.

Figure 3.5

Signal Integrity and Delay Uncertainty: Taskforce  Recommendations

SECTION 4

Design Productivity

One Taskforce objective is to find approaches to design microprocessors with fewer engineers while being concerned about more detail. There will be .2 Billion transistors and these transistors will be switching at microwave frequencies. Once these cross signal interactions are added, there are nearly of a Billion things to verify.  The problem will exceed an engineer’s ability to analyze the whole design to uncover timing problems.  Because most of the timing effects will be layout related, the functional analysis will not be effective for physical design verification.  Other analysis techniques including logic and circuit simulation, have already exceeded their limits.   Static analysis, that is based on gate or transistor verification, will overwhelm the designer with exceeding large number of false-path errors.

Design productivity is not a product goal.  Even if design productivity is very high, it does not guarantee satisfactory chip functionality.   The time it takes to deliver often depends on other critical issues such as a wrong or incomplete specification, poor design quality, or poor design practices.   Our object here is to attack these critical issues, which will in turn lead to improved productivity.

Details dominate the effort to design a chip. Many of the simplifications that we have used are no longer adequate.  However, we will still be designing microprocessor chips.  It is important to recognize that design will change in order to execute projects and EDA must change faster than design so it is ready when the problems arise.

In previous generations, designs were limited in speed by the transistors, and interconnect was second order parasitic.  In future generations, speed will be limited by interconnect and transistors will be a second order parasitics.  Interconnect will determine chip speed.  Solving interconnect difficulties will dominate design effort.  The design system and methodology must evolve with these changes.

PRODUCTIVITY FACTORS

Design productivity is a by-product of two interrelated activities.  The first is the efficiency of the team producing the design.  We observed that microprocessor design teams had a wide variation in design team sizes.  Some teams were as much as an order of magnitude larger than others.  Even factoring in design differences did not account for this wide variance.  The factor that was common to efficient design teams was that they contained  “tall-thin” designers who had worked as a team previously.

The second productivity measure is the number design iterations required in order to reach a correct implementation.   The most effective way to improve design productivity is to reduce design iterations.  One of the major causes of iterations is inconsistent views of a design as a design progresses from one software tool to the next.  Many tools add value by optimizing algorithms and adapting heuristics to maximize performance.  In a flow, each tool is self optimized but the collection is sub-optimal for the entire design iteration.

Electronic design automation must assist both of these interrelated activities. Designers’ capabilities must grow so that they are capable of working across hierarchy.  EDA needs to optimize design processes, and focus design activities, and methodology needs to concentrate the engineers’ effort on the most critical tasks.

GUIDE LIINES

We have developed a few guiding principles for creating High-end Microprocessors using 100nm processes.  These guiding principles may seem simple but their impact will be enormous.

·	Avoiding problems is more beneficial than identifying and correcting the errors later We are encouraging designers to do whatever is necessary to prevent repetitive verification.  We encourage that schema be devised that makes verification simpler.  Commonly, a cell is designed then placed and routed into a chip.  This is followed by an analysis of the interactions between that cell, the surrounding interconnections, and other circuitry.  We encourage that designers prevent problems by rules.  A typical rule may be to include buffering and shielding during the design of a cell to make it resistant to signal interference.

·	Verify once and use the results forever.  We are encouraging designers to thoroughly evaluate each hierarchy level and encapsulate it as a design entity for the level above.  The encapsulation must encompass a broad range of design parameters.  Certainly among these parameters are function, timing, signal integrity factors, power, instantaneous current, size, pinout, and design assumptions.

·	Change design to be interconnect centric. The timing of 100nm designs depends upon the interaction between signals.   Characteristics of all but local interconnections dominate over active devices.  The order of physical and electrical design must consider interconnect first then the active devices.   What we are suggesting is forecast functions then precisely define interconnections.  Use the forecasts and a precise layout to refine each function through hierarchy.

·	Tether design changes to the old versions to control the magnitude of any change.  We are suggesting that controlling the effect of a change is as important as the change itself.

Figure 4.1 Guiding Principles

In light of the guiding principles, several strawman design approaches were evaluated.  We felt that some were not capable of achieving high-speed 100nm designs.  Others would be burdened with immense details at high levels of hierarchy. The following design approach will meet the challenges of 100nm microprocessor designs.

MEET-IN-THE-MIDDLE

We suggest that a formalized meet-in-the-middle design approach will be extremely advantageous. Design will be hierarchical.  As usual, the design process begins with architectural definition and ends with a physical realization and testing schema.   The intersection of these domains is the middle.  For microprocessor design, the middle is the full chip level.  The full chip level is where the lowest level of architecture design and the highest level of the physical design meet.  (We will see later that additional “middles” can be established.)

Figure 4.2 Meet in the Middle Design Approach

AVOIDING PROBLEMS

Applying the four principles leads to some conclusions.  Avoiding problems implies that we cannot perform bottom up design without thoroughly specified goals.  Goals need to encompass the full spectrum of design parameters from delay to signal integrity and from power/current requirements to area/pinout.   The goals must be credible estimation and be as accurate as possible.   Timing information, which heretofore was a backannotated afterthought, needs to be accurately predicted and budgeted.

Figure 4.3 Interconnect Centric Design System

ESTIMATION

Budget s are a means of passing constraints down hierarchical levels.  The budgets must enable realizable designs. One characteristic of efficient design teams is the ability to estimate/forecast well. These teams have learned to estimate efficiently because they have experienced tall-thin designers who migrate across design levels. Their high level decisions are a natural outcome of low level consideration.  We suggest that estimation become institutionalized.   Special methodologies and EDA need to be developed to estimate a block of hierarchy as accurate as possible.

We foresee estimation as a joining of top-down specification and bottom-up prediction.  Prediction is never exact but the quality of the design in the middle depends on being close.   For the full chip level, it must be close enough to complete the level designed.  The design will include power distribution, built -in test capabilities, dominant signal (such as clock and reset) distribution, inter-block timing, and soft error control.

Estimating is a conjunction of historical information and tools.  Nearly every microprocessor design team has individuals that have designed microprocessors previously.  Once captured, the historical experience can be used as a starting point for the next microprocessor design.  The same is true for the large blocks (intellectual property).   We expect automatic generators will create data paths, register stacks, and memory.  (These generators can also build the models.  We expect synthesizers will create random logic.)  These synthesizers will be advanced to produce increasingly accurate models for high level verification.  Design activities may resort to prototype experiments using new blocks or models.  However, we feel that model building should be automated with special tools that confirm accuracy.

Some methodology changes will improve the quality of estimation and of the chip design - whereas, software can prevent problems by active avoidance.  One example is adding of shielding between interconnects that are likely to interfere.  This shielding stabilizes the circuit operation.  This shielding will minimize the effect of an inerconnect on surrounding entities.  It also will make it possible to accurately predict a block’s operation more accurately.  Problem avoidance reaps a side benefit of predictability.  Often, problem avoidance methodologies do take additional area.  However, the verification has already forced problem avoidance schema.  We suggest that these schemas be increasingly leveraged.

SIMPLIFY DESIGN

Some methodology changes can simplify the whole design task. Power and signal integrity will be both affected by the number of signal transitions.  Minimizing the transition counts and especially, controlling transitions on longer length interconnect will reduce power and noise problems.

With meet-in-the-middle design techniques physical design starts at the full chip level.  As was stated earlier, design needs to be interconnect centric, since Interconnect has the largest effect on design with longer interconnections having the most effect. This includes all the long signal lines, busses, global clock signals, reset signals, testing signals and power distribution.  The longest interconnections are at  the chip level then the block level interconnect and finally silicon and cell level interconnect.  To design these interconnections, the high level blocks of a design must be estimated.  The blocks must be placed in the chip structure and layers of high level interconnect that will dominate chip performance will be routed.   The blocks are thereby specified in-place where they will be used.  Care can be taken to use blocks repetitively to save design and verification time.

After chip level interconnect is completed, the block specification is enhanced with the dominate interconnect effects.  These including loading effects, signal integrity effects of crossing or nearby interconnect, clock/sequence skew, and power fluctuations.  The block’s pinout and dimensions are also delineated.  This enhanced block specification allows a team to have an intact hierarchy that is divisible into sub-activities that can be reassembled.   So each block always coexists with its environment.  As a design is successively refined, a modification within one block can be reflected to the rest of the design through the chip level hierarchy.   Thereby, the new design is tethered to the old design and degree of change can be controlled.

An advantage of meet-in-the-middle is early verification.  The estimated blocks are complete models where lower level details (behavior, delays, signal integrity, power/current, area, and pinout) are abstracted into high-level blocks representations.  Often the high level blocks will have built-in checkers to assure that function is being use appropriately.   As a design proceeds from estimation to realization, the model/verification accuracy will improve.   As a design matures, the verification is completed hierarchically.  As blocks are refined, only the modified blocks will need new parameterization and verification will be maintained.  As we have indicated, the details of the design must be captured.   Physical data (layout) needs to be used whenever available.  Engineers concentrate on the interconnect, and model the functions.  Controlling change is important to assure convergence and limiting the amount of verification.   Whenever a design modification is proposed, it is naturally tethered to the preceding design through block and chip level constraints.

MODELING

The lower levels of detail are abstracted into models that are used at different levels of hierarchy up to the blocks at the full chip level. This is reverse synthesis.   Handling detail at a high level requires elaborate modeling techniques, but handling detail in large designs has always been difficult.  These techniques trade the difficulty of analyzing a billion things for the difficulty of building models.  Verifying a billion things is a nearly NP complete problem.  Model building time and accuracy can be traded off against one another to minimize the effort.  However, automation is the answer.   For example, power can be modeled as turn-on current, reset current, clock edge current, nominal operation current, and test current.  Each element of the model requires an evaluation.  These evaluations will be automated so any entity can be rapidly evaluated and the higher levels of modeling can utilize the lower level parameters.

The chip is the border between the architecture and the physical design,  For the next lower level of design, specification and logic synthesis/design/generation is the border.  At this boundary, the process takes in the full range of specifications.  It then builds the interconnect and chooses blocks from a library of lower level components.  We do intend that physical design of interconnect be the primary task of the synthesis tools.  Interconnect will be the primary consideration in design and other design aspects must service the interconnect needs.   As the procedure concludes a full range of encapsulated models are derived for verification at the level above.

·	The four principles can be applied through a series of techniques.  We have made some observations

·	Reduce design verification by making designs regular.

·	Un-complicate design by adding microcode to reduce hardware complexity.

·	Planning power, signals, soft error handling, testing approaches, area and  pinout at the chip level makes creating detail immensely simpler.

FORECASTNG

Design methodology will change to enable 100nm microprocessor design. New design automation software is needed to support this new methodology. The first software required is to enhance the ability to forecast and estimate blocks before they exist.  The second software is required to build models that the forecaster and high level verification can use.

Forecasting is block planning based upon libraries and captured knowledge. It helps model early stages of a design and audit the later stages of design. The objective is to always building a reservoir of design knowledge while analyzing different views of the knowledge to detect design problems.  The estimation process functions by extrapolating from current available data to a design proposal.  When the extrapolation exceeds limits, more data is requested.  This data may be supplied through experience, libraries, generators, or prototyping.  As a design matures, the Forecaster audits implementations to assure that specifications are met.   It interrogates a wide range of characteristics such as: soft errors, signal integrity, power, testing, and area compliance.  If a design exceeds any bounds, the design needs to be modified as early as possible. This approach allows for successive refinement of a design and builds a multi-team concurrent environment.  For example, if the chip current exceeds the power capacity then either the power rails must be redesigned or the chip must be re-architected to reduce power requirements.  The Forecaster is key element in interconnect centric design environment where interconnect is designed first with estimates of  the functional blocks.  This code must extract signal interference, block timing uncertainties, and power consumption from the physical design.

Figure 4.4 Forecasting

Another key element allows estimation and knowledge collection.  The design automation process that we are proposing requires many models be generated rapidly.  Therefore, an Automated Model Builder is paramount for a productive design environment.  Without this capability designers may be a trade-off of design efficiency against  modeling expense.  This would lead to no net gain in productivity.  The Automated Model Builder will absorb the physical design characteristics for all the levels of design including the chip.  It abstracts lower hierarchical level information in a form that high level hierarchies can use.  This extraction covers the full range of design parameters including signal interference, block timing with uncertainties, and power consumption.  The block level needs to handle enhanced delay variability do to the uncertainties of circuits and in the logic paths.

Figure 4.5 Automated Model Builder

The Taskforce proposes significant changes to design methodology and design automation.  These changes are directly forced by 100nm processing.  These changes are also forced by microprocessor design continuing to grow in complexity which has magnifies the need for productivity.  It is built on the following set of principles:

·	Avoiding Problems

·	Verify Once, Interconnect Centric Design

·	Tether Design Changes.

The Taskforce feels that effort will need to focus on these new methodologies and design automation as early as possible so we will be ready for the challenges ahead.

SECTION 5

3.5GHz  / .2Billion-Transistor Production Testing

The Taskforce examined the test requirements for the 100nm / 3.5 GHz Microprocessors. Test is required to discard parts that have manufacturing defects.  Most important aspects of testing are: manufacturing test, as well as design and EDA requirements for test planning, and design for test (DFT).  The Taskforce concluded that industry can’t afford to continue to approach test from a business-as-usual point of view.  There will never be again a generation of testers that can test a chip the current generation do.  Furthermore, test will impact design and will have to be resolved at each step of the design process.

While many aspects of test will scale with feature size at 100nm, other aspects will require new development and approaches.  The following overall impacts must be considered:

With chip clock frequencies moving to 3.5GHz, and with edge-rate frequencies moving well beyond that, target testing frequencies and complexity of test head circuitry will require significant increases in both manufacturing test hardware cost and complexity.  Some present test approaches will have to be abandoned.  For instance, it is highly likely that parametric testing, edge rate testing, and other key test approaches will be largely replaced by moving both test hardware and the tests on chip.  Forecasts indicate that test hardware will approach $100M per fab.

Current conclusions concerning 100nm interconnect parasitics (complex distributed R-L-C-M due to coupling and over-the-cell routing) is that interconnect timing and parasitics test issues will have to be completely dealt with at design time.  The Taskforce believes there is little that can be done during test to reliably detect this type of marginal manufacturing defect, regardless of the test hardware used, including on-chip.  This is due in part to those effects taking the form of signal-combination-specific minor changes in timing and signal levels.

The Taskforce analyzed each of the basic types of test for 100nm impact and issues. Taskforce reviewers felt fundamentally there were no new issues in either structural testing to detect if all the blocks are interconnected, or in functional testing to verify if all the blocks are performing properly.  On the other hand, there are significant issues in the huge size of the chip circuits to be tested, the huge number of test vectors needed, and greater complexity of target chip architecture, that will have to resolved for 100nm test. Fortunately, chip I/O pads counts are forecasted to move to 4000 pads with the number of registers and latches historically forecasted to grow proportionally. Test generation complexity should therefore be difficult but doable.  Some issues to be resolved are expected to include on-chip storage of vectors and results, partitioning of the chip into separately tested major blocks, test of separately procured IP blocks, and balancing long vector sequences with reasonable test times.

Growing SIV threats is expected to lead to far greater use of error detection and correcting hardware, software, and microcode.  The Taskforce and other reviewers feel this area is roughly adequately solved.

The growing impact of interconnect parasitics and other errors and the difficulty to handle them during either design or manufacturing is expected to lead to far greater use of error correcting, etc., hardware and architecture. Taskforce reviewers felt that such approaches to hardware architecture and design discipline were adequately known to handle 100nm requirements.

Unfortunately, test issues resulting from the impact of timing at 100nm are all felt to be unresolved.  This includes, for example, test approaches for handling effects of signal coupling interference on both delay and signal level, soft errors, noise, and transmission line effects.  For those classes of effects not handled fully during design, new fault models and test approaches will be needed.

Design For Test (DFT) for 100nm will therefore need to be extended for all the above test issues that are currently felt to be understood.   A significant, albeit straight-forward effort will especially be needed to handle the much larger number of circuits, nets, and input and output vectors for 100nm chips.  This effort is expected to include far greater use of scan and built-in test.  However, completely new approaches will need to be developed for issues such as timing that are felt to be completely unresolved.

The following sections discuss the important challenges and trends that will impact test for 100nm.

EQUIPMENT COST CHALLENGES

With feature size rapidly reducing and with wafer and die sizes remaining the same,  manufacturing cost per transistor is declining rapidly.  Unfortunately, with the clock frequencies and chip density climbing, test equipment depreciation per transistor is forecasted to remain flat.  Figure 5.1 shows these two relationships both historically and as forecast by the NTRS and other industry information [ref to earlier Gadi Singer presentation.]

Fig 5.1 Test Cost Impact on Product Pricing

TEST YIELD CHALLENGES

Product requirements and feature size scaling will result in silicon speed increases that will increase faster than the required increase in overall timing accuracy (OTA) of manufacturing test equipment.  The figure 5.2 shows these two relationships both historically and as forecast by the NTRS and other industry.  Note that design and EDA are also expected to have to require far greater accuracy in their methods in order to properly handle high-end product timing requirements for more complex interconnect parasitic signal integrity.  Manufacturing test use of increased guard-banding against timing defects to compensate for the loss of timing accuracy will result in a finite and significant manufacturing YIELD LOSS.  Without any real change in manufacturing, quality will be reduced.  This yield loss will be in addition to the impact of other unmet 100nm design and manufacturing paradigm shifts.

Figure 5.2 Yield Loss due to Guard Banding

BURN-IN CHALLENGES

With the increased number of:  chip input/output pins, increased supply current, increased power dissipation, and rising chip-to-substrate interconnection complexity, the cost per burn-in socket is expected to rise sharply.  In addition, alternatives to uncover potential chip manufacturing failures, e.g., use of Iddq testing, are at risk for use in the future. The figure 5.3 shows these two relationships both historically and as forecast by the NTRS and other industry information (ref to earlier Gadi Singer presentation.)

Figure 5.3  Cost  Per Burn-in Socket  Position

TIME-TO-VOLUME CHALLENGES

Increased silicon complexity can significantly extend test. Since one key contributor to lower, more competitive product pricing is product manufacturing volume, Time-to-Volume is as important as initial product release and overall Time-to-Market.  This is especially true for products targeted at low end, high volume markets. The below figure shows these two relationships both historically and as forecast by the NTRS and other industry information.

Fig 5.4 Time to Market and Volume Increasing

WAFER PROBING CHALLENGES

While pad count forecasts for 100nm are modest compared to the growth of on-chip complexity, new probing technologies will be required for 2000 plus pads.  Issues in wafer probing include dealing with pad spacing, and contact pressure and reliability.  Power supplied to the pads will be increasingly difficult, both with respect to lower supply voltages, regulation of voltage onto the chip, greater supply currents (both supply and ground returns).  With much higher power dissipation, thermal control of the chip during probing will be an issue.  Finally, probing will have to deal with requirements for probe performance, especially in the areas of bandwidth and noise.

A related critical issue will be outgoing quality from the standpoint of defect elimination that results from test applied during wafer sort.  At 100nm high clock and signal frequency and edge rates, at-speed test and speed sorting will be quite difficult both to set up and perform.  With chip timing being much more critically dependent on much more complex parasitics (timing stemming from R-L-C-M coupled and over the cell route parasitics vs. today’s lumped-C parasitics), accurate measurement of related process parameters is expected to be needed at this test step.  With higher power and supply currents and related more complex packaging, it will also be important to have integration of wafer probing with accelerated stress and reliability screening.

GENERAL METROLOGY CHALLENGES

A number of test challenges are expected to arise in the overall area of metrology related to manufacturing test.

Test seeks to establish if the devices are alive and structurally interconnected correctly once the product has been manufactured.  The classic test and DFT approach applies here, that of ensuring that the design has adequate controllability and observability.  There is fundamentally no new ground to cover here.  There is, however, the impact of complexity of coming 100nm advanced processor chips.  They are extremely Large, with a greater number of circuits to scan, and, therefore, larger numbers of vectors needed will be needed.  Test at 100nm will need to consider approaches which partition the chip for better handling of  the larger amount of scan, including possibly storing vectors on-chip.  More complex and dense high end processors means new architectures, increased use of power moding, and greater use of complex instructions.  Product projections also forecast new complex, possibly-mixed-domain chip designs, for example following the product directions similar to MMX and high-performance multi-media partitions on-chip.

There will be an increased difficulty to access to internal nodes for measurement.  This will stem greater physical design use of  multi-level interconnect, as there will be increased need for routing into blocks to access to lower levels of the local design hierarchy.  It will also stem from the 100nm ultra-fine-line physical geometry needed for interconnect and devices.  Packaging is expected to be predominantly flip-chip, with “access” from the back of chip desirable.  Measurement environments will be more complex, for example, e-beam probe techniques will need to be done using a vacuum.

Greater measurement accuracy is expected to be required.  Areas especially difficult will include the parametric intrusion from probing (e.g., loading due to the required micro probing), and the difficulty achieving the resolution of critical parameters, for example, as required to establish on-chip pico-second timing stemming from the extreme clock frequencies and signal edge rates.

Metrology will also be a challenge. There will be greater time required data acquisition. .With the very large device counts, growing number of registers, and more complex architecture; greater time will be required for problem location techniques (“needle in a haystack”).

IMPACT OF TEST CONDITIONS

An important 100nm test challenge to resolve will be to establish if parametric stress conditions can help to distinguish defect behavior from normal behavior, for example, the use of temperature stress or voltage stress in finding defect devices.  The figure 5.5 shows example data illustrating the possible roles of parametric stress testing in manufacturing testing.

Fig 5.5 Temperature and Voltage Stress Identifies Faulty Behavior

BUILT-IN-TEST

This part of test focuses on establishing if  all the blocks of the design doing their intended function correctly once the product has been manufactured.  The functional test issues here concern the greatly increased chip and block density and complexity, higher speeds enabling new, denser and more complex architectures,  growing time in test, and the attendant need for quality for these new more complex products.  The above are believed to be “roughly solved”, especially if new more complex functional designs are accompanied by early test planning, including appropriate test, BIT, and BIST hardware, and providing specific means to efficiently do functional testing during manufacturing test.

TESTING OF CHIP TIMING

The Taskforce believes that there are no identified approaches that can provide useful validation of chip timing during manufacturing test.

This also means that there is believed to be no reliable way to detect all unresolved chip timing problems during manufacturing test.  The issues that lead to these conclusions stem from the difficult of 100nm manufacturing test to deal with on-chip noise that could cause signal errors.  In addition, there are currently no test approaches to handle all the combinations of active devices, nets, signals, and nature of combinations of geometry (e.g., neighboring and  over-the-cell routes).

Reliable fault models will need to be developed for all of the types of net and signal interferences, including complex R-L-C-M parasitic coupling, and fault modes for both over and through the cell routing.  Similarly, new fault models may be required in order to adequately handle soft error testing.  Note that many soft error scenarios conclude that it will not be possible to completely forecast the nature of soft error chip failures.

Because of these conclusions, the Taskforce believes that at 100nm, we will have to rely on Design for Test (DFT) and Built In Test (BIT) to properly handle testing for chip timing.  Even then, BIT and BIST are expected to challenging if the testing is done at clock rate speeds.

Finally, fundamental on-chip timing issues remain for such items as performance of the SCAN hardware itself, handling of clock jitter, timing issues of ECC hardware and architecture.

SECTION 6

EDA System Structure

As the number of tools increases and the kinds of data that have to be passed between tools increase, EDA tools must become software components, and API centric. Two trends are coming together which makes this happen:

The first trend is that the number of tools will increase along with the number of design issues.   The levels of design abstraction will grow.  This will be coupled with a steady increase in the data shared between tools. This indicates that designers will need to use more tools.   We expect an evolution of our EDA  design environments.  They will need to be more than mere collections of tools, but rather tightly integrated suites of tools that explicitly support design flows.

Data needs to be managed consistently through tool flows, without forcing an explosion in the number of file formats. Net, Pin, Cell and Instance names tend to be passed from the top of the design hierarchy to the bottom, passing through all tools.  Parasitic information is passed from the extractors to timing analyzers and simulators, bottom-up. Constraints are propagated and enhanced in detail as they pass from floor-planner to synthesis tools to placer to global router to detail router.

Figure 6.1 API Centric EDA

As the number of tools grow and the size of our designs grows, this has lead to three problems:

·	The number of tools that need to access any particular subset of the design data has grown.

·	The sizes of the design databases have exploded as a function of design-complexity x number of representations x number of formats generated by translators.

·	When a tool changes any datum in it’s output, it usually has to replace the entire file (or the translators will replace their entire outputs even if the originating tool knows how to incrementally update it’s database).

Fig 6.2 Component Object Systems

Using Component Object Interfaces (e.g. CORBA, COM, Java Beans) ameliorates some of these problems because:

·	There is one set of access code for each interface rather than for each tool x each format.

·	The size of the design database is proportional to design-complexity x number of representations, there only needs to be one format for each kind of data’s external storage format.  This also saves processing time because once a tool creates a datum, any tool can access it by calling the correct API without processing any unneeded data.

·	Any incrementally updated data is immediately available to any downstream tools.

The second trend is based upon the tendency of CAD tool developers to use generic operating system services to the full extent possible, but not to allow the lack of such a service to limit the power of their tools. For example, early EDA layout editing tools had tool specific code for rendering the shapes in a layout, while most current tools use X-Windows or MFC code to perform these services.

Access to design data has also benefited from use of operating system services, but the access model will change as tools shift to the use of component objects.

Currently, most tools communicate their data by exchanging files. Each tool outputs its data into a file  (in a de facto standard format, a public standard format or a proprietary format).  This causes four problems:

·	Each tool that needs to access the design data has to read the entire design file, and process all the data in the file (even if it only needs a small subset).

·	If two tools that do not process the same file format need to exchange some design data, they need a translator program to map the data from one tool’s format to the other’s, after which the second tool will read it all again.

·	Often a new version of a tool,  we usually find that it has added new information or structure to it’s file format so we need to either: (1) Find a new revision of the receptor tools that accept the new format. (2) Revise the translator to accept the new format.(3) Write a new translator to map the new format.

·	Providing a multi-tool accessible file format imposes a heavy extra burden on it’s developers: (1) They must provide documentation of the public format that is sufficient for people to write readers and writers in other tools.  (2) The need to try to minimize changes in public file formats so as not to impose too heavy a maintenance burden on their users.

Object Interfaces eliminate these problems.

·	A tool that binds the interface can read only erlevant data that it needs and not irrelevant data.

·	The provider of the interface maps the file data to the interface so each tool that binds the interface uses the same code to access the file data.

·	Interfaces are themselves versioned so if a tool changes a file format, it may support both the old version of the interface and the new version. This means that tools that depend upon the old format don’t break when the new tool comes on stream.

·	There are already a large number of support tools that help an interface supplier make it accessible to potential users.  In addition, the versioning helps to reduce the impediment to evolving tools

The combination of Component Object infrastructure, and the expansion of EDA tools, needs the kind of services that this structure affords.  The result  will provide users suites of flexible tools, involving few translation steps, and evolve rapidly.

SECTION 7

A Vision of 100nm Microprocessor Design.

The Taskforce has identified transitions that will occur as we attempt to design custom-chips  that are built in silicon processes with geometries less than 100nm and which operate at GHz frequencies.   We have discussed ways to mitigate new effects by judicious changes in processing, design methodology, and design automation. These innovations will be essential in order to meet these design challenges.

PROCESS ENHANCEMENTS

The Taskforce has identified signal integrity as a major challenge.  Signal distortion levels will increase as a result of power transients and inter-signal transfers.  Signal Integrity is a problem in the minute. There is an enormous group of details that arise concurrently to upset or retime signals.  An engineer cannot concentrate on details when there are Billions of details.  Therefore, the challenge is in the handling of details while efficiently doing design.  The most effective technique of controlling inter-signal interference is by shielding and by using power planes to supply primary current to the chip.  These techniques should be expected since they have been used in PWBs and MCMs for years.  It is not a matter of designing around signal integrity.  There are too many problem sources for that approach.  A methodology change is needed to remedy this problem.  We need to change the characteristic of the problem.   We need to be able to deliver hundreds of amps to sections of the circuit instantly.  The signals on the bus lines need to be stable in a determined amount of time and not have bus signals with wide variations in delay.

The upside benefit of adding layers of metalization is design efficiency.  The downside is a significant increase in processing cost.  However, other solutions to signal integrity require spreading the elements of a design further apart.   This also requires larger chip area at substantial costs.   Additionally, the di/dt on power lines, clock, bus and other long high fanout interconnects will be substantial, and the inductive as well as the mutual inductive effect will be dominating.   The Taskforce recommends that the one power distribution layer be expanded to as many as four layers of metal.  Two of these layers will serve as power and ground planes.  Two layer as interconnect shielding and block shielding.

The power and ground planes should be adjacent to each other with a maximum capacitance between the layers.  This will reduce power spikes but additional suppression will most likely be required.  The capacitance between power and ground will need to be capable of sustaining voltages for as long as a nanosecond while the power surges reach hundreds of amps.    That implies that a large capacitance is required.  The Taskforce recommends that process technology either build a large integrated capacitor into the chip or use MCM technologies to attach an array of capacitors to the chip.

Figure 7.1  Process Modifications

Later soft errors that result from either alpha particles or charged particles will be discussed. Soft-errors are random nondestructive events resulting in recoverable circuit error, which are caused by the induced noise from subatomic particles. When the prevalence of signal upset is high enough, processing must find a means to harden circuits against soft errors.  SOI is one method for achieving hardening.   SOI has, also, the potential of being a superior high frequency technology.  We do not want to minimize the risks that this conversion may entail.  We only suggest that we may be forced into this space and the technology must be ready.

METHODOLOGY ENHANCEMENTS

Chip design methodology will require even greater changes.  The objective of design is the development of a chip or chip/system that is functionally working, and that meets performance requirements in a predictable amount of design time.    100nm designs are more complex than previous generations because many details that will overwhelm design, because there will be more transistors to design and because designs will not converge without a strategic plan.

The Taskforce recommends that designers use a meet-in-the-middle approach.  This approach uses some rigged hierarchies as the basis for design. The hierarch is architectural definition and lowest depth is physical layout and test.  The middle is full chip level where architecture design meets physical design.

The Taskforce believes that an increasing amount of design will be accomplished at the full chip level.  This may include global optimizations like using many staggered clocks or asynchronous logic or minimize the number of signal transitions.

As we have indicated,  interconnect will dominate over semiconductor delays. Design will become interconnect centric. Because the longest interconnections are between blocks, this part of the physical design must be completed first.  The rest of a design will flow from the decisions made at this level.  To make these decisions, a design engineer will estimate the characteristics of functional blocks in an analogous manner to the way an engineer estimates interconnect today.

We encourage rule-based design constraints.  A typical rule may be to include buffering and shielding in a cell to make it signal interference resistant.  Verification at the full chip level is reaching the end of its useful life.  At the full chip level, there is just too many things to verify.  Prevention and techniques to avoid predicaments must become the approach.  From a timing standpoint, timing delays and the delay variability will be determined at low levels of hierarchy and abstracted into forms that can be applied at higher levels.  The same approach is necessary for power and transient power, for test and built-in means of testing at speed, and for physical characteristics such as area and pinout.

In order to generate a block, its function is specified.  Commonly these functions are synthesized or compiled into low level blocks that are then placed and routed. In GHz chips, however, physical design however predominates over function. The function has degrees of freedom to allow the other constraints to be met.   It is common to see similar system architectures be designed with different functional blocks.  Therefore, the Taskforce recommends that low level design be considered a physical design task with constraints. Verify, at this level once then repeated use abstractions at other levels.  One of these constraints is a high level functional specification.  At the completion of the low level design, a designer needs to build a higher level block-model that abstracts the detail but maintains the essential fidelity required to assemble blocks.  It is at the block level, where the full chip level will be assembled and verified.  The Taskforce believes that design convergence is a function of attention paid to initial specification, attention to detail at the lowest level of hierarchy, and attention to abstracting the low level of detail (including physical back annotation) to a chip level block.  As blocks require iteration then the change should be tethered to the old circuit to reduce the magnitude of the verification effort.

High level decisions are a natural outcome of low level considerations.  Low level development is driven by chip level budgets.  These budgets will set the realizability of a design.   So to begin a design process, an engineer will need to estimate or forecast the characteristics of the block being considered.  The characteristics should include power requirements, built -in test, inter-block timing, and signal integrity factors.  These factors will be assembled from archived designs and from modeling or prototyping efforts.

Figure 7.2  New Design Methodologies

ELECTRONIC DESIGN AUTOMATION

New categories of design tools will be needed to create custom-chips that are built in silicon processes with geometries less than 100nm and which operate at GHz frequencies.  The tools can be grouped into two categories.  The first category is tools that improve a particular level of design.  The second category is tools that improve inter-level design.

Captive design support activities and commercial EDA software companies have vigorously developed design automation in the first category type.  These EDA activities are numerous and they often invent new solutions for particular design problems.  In fact, as we have expounded, there are new design problems that require solutions. We reiterate a few examples here.

Power and supply current analysis must take into account: average as well as instantaneous surges.  This analysis must determine how high power will effect signal integrity and thermal variation in delay.

Another requirement is for multi-path with multi-signals timing analysis.  Because delay is a function of history as well as relationships between signal directions, a new class of timing analyzers is required to verify circuit operation.

Placement/Route controls signal integrity, and power and minimizes the number of signal interactions. Design automation needs to call upon noise immune technologies such as exploitation of shielding, repeater/receiver hysteresis and transition slew rate control.

Physical design generators for arithmetic as well as other functions need to combined synthesis/placement/routing for inter-block connections that are signal-integrity sensitive that exploits other techniques to improve noise margins. Rapid regeneration of predesigned blocks (cores) using constraints for aspect ratio, timing, power, noise, etc.

Microprocessor design will increasingly be large software projects coupled with the very regular hardware design.  New code generators needed to enable the hardware to make better use of regular structures. The design approach needs to be switched from local repair of problems to global avoidance.

Delay fault testing will be necessary to uncover behavior modifying processing irregularities.  EDA will identify metalization edges that are most  to cause timing errors and multiple paths which need to be exercised to verify working parts.

These are real challenges that the Taskforce feels that the industry will naturally find solutions.  EDA has been capable of generating this class of solutions in the past and we have faith that this trend will continue.

It is the second category that improves inter-level design where EDA has not been generally successful.  Inter-level implies multi-disciple, which often necessitates the integration of software that was never intended to co-exist.   As part of our preparatory tasks, this Taskforce reviewed the results from previous taskforces on EDA.  Each one identified that integration was the most important task ahead.  However, integration has been achieved with very limited success.

Now, this Taskforce is recommending that we change the picture of integration.  We recommend that EDA become interconnect centric.  Interconnect dominates. When a function is synthesized or compiled it is compiled so that the physical constraints are met.  This is not sizing a buffer for a particular gate fanout.  The integrated functionality must understand the signal’s route, and its effects on power, signal integrity, then assign buffers and shielding along the path to balance the electrical and footprint design requirements.   It is tying detailed analysis to the configuration of electrical building blocks.  It is living by rules that prevent the need for endless full chip verification.  EDA has created spheres of excellence.  As long as each EDA sphere orbits at its own rate, alignment will be infrequent.  Alignment must be designed into the system.   We are pessimistic that EDA can be interfaced into alignment.  We are pessimistic that EDA can be assembled into alignment.

Alignment for chip design and EDA requires a concerted methodology.  There are Billions of  elements of data.   EDA software structure must be build on a strong base of information flow.  An EDA systems productivity, and reliability will depend on using API interfaces.

The Taskforce further recommends that EDA software architectures incorporate a new set of tools.  These tools aim at the same interconnect centric goal from another view.  The Interconnections that are most dominate are the longer lines that interconnect blocks or carry global signal such as clocks and busses.  These interconnections are so important that they need to be known before defining lower level details.  They determine delay and skew between events. They are the largest single power consumers.  Their length and proximity to other interconnect and active devices causes signal integrity problems.  They will need to be designed first.

However, for interconnect to be designed, there has to be a set of functional blocks to connect.  Therefore, the design process will initiate with estimation of the blocks that will later undergo detail design.  We suggest that EDA create an ability to forecast block design.  This capability will be built upon libraries, archived design data, synthesizers and generators.   This is a special case of rules driven design where each class of blocks will adhere to rules.  For example, if it is a memory, then do ___ ; if it is a register stack, then do ___; if it is a decoder, then do ___.

The forecaster value will depend on the design activity’s ability to collect knowledge and build models.  The models will map lower level detail into high level design.  The high level design must deal will models for signal interference, block timing with uncertainties, and power consumption. The model builders will need to extrapolate from libraries, prototyping, or generators.

The Taskforce further recommends that verification be built into the design process. Rule base audits are very effective. An auditor queries implementations as they are created to avoid problems.  It will interrogate the full range design space: signal integrity, power, testing, timing, and area compliance.  Difficult situations will be eliminated before they cause major design iterations.

Figure 7.3  Interconnect Centric EDA

We are recommending that EDA be revamped to make it interconnect centric.  The Taskforce dares to ask software to begin again.  For those who question if this is needed, let us examine EDA history.  What happened to: Tegas, Calma, Daisy, Valid, Crosscheck, Scientific Calculations, and Silvar-Lisco.  EDA is change. The only question is who will fill the void.

SECTION 8

Future Research

The EDA Roadmap Taskforce has encountered a number of challenges that require further research.

SOFT-ERRORS

Soft-errors are random non-destructive events resulting in recoverable circuit error, which are caused by the induced noise from subatomic particles. The perturbation caused by the particles interacting with silicon atoms can cause the value of a storage cell to change if the induced charge goes above or below a fixed level (Qcritical). Further, transient output pulses in combinational logic circuits may indirectly produce changes in the state of other circuits if they occur at critical time periods, such as during clock or data transitions. There are two sources of these subatomic particles:

Alpha particles — high mass particles which result from the radioactive decay of materials within the IC or its contacts. Alpha particles can produce a great amount of ionization along their track, thus liberating large numbers of electron-hole pairs from atoms over a very short distance. If free electrons are captured on a capacitor charge plate, the memory state may be flipped. Also, transient output pulses may result on signal lines that indirectly produce changes in the state of circuits if they occur at critical time periods, such as during clock or data transitions.

Cosmic particles — high-energy particles which emanate from outer space. High energy cosmic particles can fracture the nucleus of silicon atoms thus causing a stream of secondary particles that can produce a great amount of ionization, thus liberating large numbers of electron-hole pairs from atoms over a very short distance. If free electrons are captured on capacitor charge plate, the memory state may be flipped. Further, transient output pulses may result on signal lines that indirectly produce changes in the state of circuits if they occur at critical time periods, such as during clock or data transitions.

The probability of a soft-error occurring on an IC is a function of several factors making it difficult to quantify. The materials' properties, the altitude under which the IC must operate, and other shielding each effect the probability of a particle strike. The feature size and feature packing, as well as the design itself effect the probability that a strike will cause an event upset (or soft-error). Whether or not an occurring soft-error impacts the execution of the IC is a function of whether or not the bad state is used before it is refreshed to a correct state. All told, the probability of a soft-error that affects machine operation is extremely small, but it is increasing as ICs shrink. Even with a low probability, it is an area that deserves attention as a single error occurrence could cause the machine (using the IC) to crash or produce incorrect results. The probability of a soft-error occurring on an IC is a function of several factors making it difficult to quantify. The Taskforce has evaluated several studies and has concluded that the exposure to soft errors is not determined.  We need further research on soft error rates.  If soft errors are once a year phenomenon, then rebooting a computer is practical.  If it is once an hour phenomenon, it deserves attention as a single error occurrence could cause the machine to crash or produce incorrect results.

To understand the impact of feature size on the probability of soft-errors, the following should be considered. The charge of a memory device is approximated by Q=CV, where C is the gate capacitance and V is the voltage differential. Gate capacitance is approximated by C=(GOXAgate/)/TGOX, where GOX is the dielectric constant for the gate oxide (3.9 X 8.855)10-14 F/cm for SiO2), Agate is the gate area (which scales as the square of the feature size), and TOX is the oxide thickness (which scales with feature size). Thus, the gate capacitance (given no change in materials properties), decreases proportionally with feature size.

The relationship of charge to the Technology Roadmap is given in the following graph. As shown, the state charge for latches and RAM is decreasing as a result of decreasing feature size and Vdd.decreases by 62.6% by the year 2003. Since the charge on an electron is constant, this implies that the relative number of free electrons resulting from ionization decreases by the same percentage. Therefore, as an approximation (given no changes as a result of materials properties) the probability that a particle strike will cause an event upset might be expected to increase by the same proportion.

Figure 8.1 CMOS Charge is Decreasing

Another observation that can be made is with respect to the probability that a strike will cause multiple event upsets, that is, a single particle strike upsetting multiple memory states. The probability that free electrons will be captured by a transistor gate capacitor is a function of the distance between them and the gate. As the density of ICs increases, the spacing between transistors decreases, thus increasing the probability of multiple-event upsets from a single particle strike.

The effect of subatomic particle strikes and soft-errors is not new to IC design. It is a phenomenon that has had attention in memory design, where parity detection and error correction is now accepted practice. However, it deserves further research and consideration with respect to future microprocessor design, because of decreasing feature size, increasing feature density, and increased amounts of "on-board" memory. There are two areas of consideration for soft-errors — prevention, and detection and correction.

Prevention of particle strikes may be improved by the use of materials within the IC that result is less radioactive decay and shielding the IC. Shielding the IC from cosmic particles is not practical given the extremely high energy levels. Shielding transistor gates from the free electrons that result from particle strikes may be improved by process technology such as silicon-on-insulator (SOI). With SOI, the oxide insulator can reduce the number of free electrons that are in close enough proximity to the gate to be swept up.

Figure 8.2 Soft Errors in CMOS and SOI

Detection and Correction must necessarily be designed in since soft-errors, by definition, are not hard physical defects. Therefore, it is expected that there will be increased use of parity checking and modular redundancy in microprocessor designs. Additionally, there will be more use of error correcting schemes that can correct for both single and multiple-event upsets within a functional unit —such as a memory word or register.

In order to provide EDA support of design with the above considerations in mind, the following list of EDA research and development will be necessary:

Detection/Correction Logic Insertion

Similar to the productivity advantages to supplying scan-register insertion tools in today's EDA systems, in the near future, automatic insertion of soft-error detection logic will be desirous. Quite possibly, this support would allow the designer to identify susceptible functions (or regions) within a design and the detection technique (parity, modular redundancy, etc.) to be used, and allow computer automation to insert the correct detection circuitry.

Similarly, research into computer automation to insert correctly functional logic to process error correction techniques (with standard techniques such as Hamming codes, etc. available to the user) is desirable.

PHYSICAL DESIGN

Physical design considerations can effect the probability of multiple soft-errors within a design as well as the effectiveness of modular redundant design for detection. Physical separation of circuits from their redundant copy or bits in a register will be an important consideration for effective placement algorithms. Further, computer analysis of the density of latches and memory in regions of the IC will be important to understand the overall susceptibility to multiple-event upsets.

MODELING TOOLS

Research has shown that the critical charge level (Qcritical) is a function of the variances in a number of process variables such as doping levels, spacing, and current levels. Further research and development of accurate and efficient modeling and simulation tools that can predict the probability distribution of soft error susceptibility across regions of the chip will be required. These tools must consider the 3-sigma process variations, feature size and spacings, frequency, etc.

ASYNCHRONOUS DESIGN

With the rise in power and especially with the instantaneous current surges that occur at clock edges, it will be increasingly important to disperse circuit switching times. One approach to reduce these periodic surges is asynchronous design.  Asynchronous design has fallen into disuse because synchronous design has been greatly automated.  Research is needed to automate asynchronous design.   A different approach to timing analyzers will be required.  Synthesis will require enhancement and testing approaches will need revision.

MEASURE DESIGN EFFECTIVENESS

As the Taskforce evaluated design data, it became apparent that design efficiency and productivity are not measured.   Often one organization’s productive environment will be less effective than another organization’s unproductive design.  It is beyond a matter of expectations and perception.   We need to develop methods to measure productivity.  Likewise we need measures of quality that determine how a design compares to criteria that are created for a process and machine architecture.

FUTURE TASKFORCE ACTIVITIES

The EDA Roadmap Taskforce has investigated Highend Microprocessor  design.  We identified other market segments.  These market-driven studies may lead to different conclusions.  We recommend that two additional committees be assembled simultaneously.  One committee should study High End Standard Cell ASICs.  The other committee should study Battery Powered Communications.

When staffing these committees the most important factor is identifying individuals to lead the committees with industrial backgrounds that is heavily weighted toward theoretical work.  The leaders should have previously demonstrated an ability to lead volunteer organizations.    These individuals must be personally committed to the technology, the Taskforce objectives, and to the other volunteers.  They should build very active committees that meet physically together monthly.  This Taskforce found the greatest attendance at meetings that were held in the Silicon Valley.  Even the attendees that resided outside this area were more prone to attend meetings held in Silicon Valley.  The sponsors must be willing to cover expenses of the committee’s operation.